###### RCRA Contingency Plan

Perma-Fix of Orlando, Inc.

10100 Rocket Blvd.

Orlando, Florida  32824

EPA ID No. FLD 980 559 728

HW Permit No. 26916-HO-004

revisions by

Victor L. San Agustin, P.E., C.H.M.M.

Perma-Fix Environmental Services, Inc.

10100 Rocket Blvd

Orlando, FL  32824

August 22, 2006

TABLE OF CONTENTS FOR

CONTINGENCY PLAN

PERMIT APPLICATION SECTION NO. II.A.4.b

SUB-SECTION

NO. 		TITLE NAME 						PAGE NO.

1.0 		INTRODUCTION 	2A-14

2.0 		GENERAL INFORMATION	2A-14

3.0 		EMERGENCY SERVICE ORGANIZATION	2A-15

4.0 		EMERGENCY COORDINATORS	2A-17

5.0 		AREAS AND MATERIALS- POTENTIAL HAZARDOUS	2A-17

5.1 	Container Storage Unit	2A-18

5.2 	Waste Fuel Removal and Blending Process	2A-18

5.3 	Waste Fuel Tank Storage	2A-19

5.4 	Wastewater Tank Storage Unit	2A-19

5.5 	Wastewater Treatment Process	2A-19

5.6 	Consolidation Areas 	2A-20

6.0 		IMPLEMENTATION OF CONTINGENCY PLAN	2A-20

7.0 		EMERGENCY PROCEDURES	2A-21

7.1 	Responses to Fires, Explosions, and Releases	2A-23

7.1.1 	Container Storage Unit	2A-23

7.1.2 	Waste Fuel Removal and Blending Process	2A-24

7.1.3 	Waste Fuel Tank Storage Unit	2A-25

7.1.4 	Wastewater Tank Storage Unit	2A-25

7.1.5 	Wastewater Treatment Process	2A-26

7.1.6 	Consolidation Areas 	2A-26

8.0 		EMERGENCY EQUIPMENT 	2A-26

9.0 		EVACUATION PLAN	2A-27

TABLE OF CONTENTS

FOR

CONTINGENCY PLAN

PERMIT APPLICATION SECTION NO. II.A.4.b

(continued)

Figure No. 	Figure Name

II.A.4.b-l 	FACILITY SITE LOCATION MAP

II.A.4.b.-2 	EMERGENCY SERVICE ORGANIZATIONS MAP

II.A.4.b.-3 	FACILITY LAYOUT

II.A.4.b.-4 	CONTAINER STORAGE UNITS

II.A.4.b.-5 	WASTE FUEL REMOVAL AND BLENDING PROCESS

II.A.4.b.-6 	WASTE FUEL BLENDING AND STORAGE SYSTEM

II.A.4. b.-7 	WASTEWATER TREATMENT AND STORAGE SYSTEM

II.A.4.b.-8 	FACILITY EQUIPMENT LAYOUT

II.A.4.b.-9 	EMERGENCY EQUIPMENT LOCATION MAP

II.A.4.b.-10 	EVACUATION ROUTES

TABLES

TABLE NO. 	TABLE NAME

II.A.4.b.-l 	EMERGENCY SERVICE ORGANIZATIONS PHONE NUMBERS

II.A.4.b.-2 	SEGREGATION TABLE FOR HAZARDOUS MATERIALS

II.A.4.b.-3 	WASTE STORED AT PERMA-FIX OF ORLANDO

II.A.4.b.-4 	EMERGENCY AND PERSONNEL SAFETY EQUIPMENT

CONTINGENCY PLAN

1.0 	INTRODUCTION

This document is prepared for Perma-Fix of Orlando, Inc. (PFO) to comply with state regulations for facilities seeking a permit to manage hazardous wastes.  The regulations require such facilities to insert into the permit application a copy of the contingency plan to be reviewed by the Florida Department of Environmental Protection (DEP) and approved with the issuance of the corresponding permit.  Once the permit is issued, the permitted facility is required to provide a copy of the contingency plan to emergency response organizations likely to respond to incidents at the facility.  This document is designed to provide helpful information about installations and potential hazards to emergency personnel responding to incidents at the facility, as well as to instruct facility personnel on what steps to take in case of emergency incidents.

This document contains plans and procedures established at PFO to minimize hazards to human health, property, and the environment in case of spills, fires, explosions, or other incidents that may release hazardous waste from storage and treatment units at the facility.  Hazardous waste is a waste that may pose a hazard to human health, property, and the environment if released from a controlled environment.

Plans and procedures in this document include information on emergency service organizations, assessment of potential dangers, decision criteria and implementation methods for the contingency plan, emergency procedures, an evacuation plan, and a list and location of emergency equipment.  This document also contains the names of persons responsible for coordinating emergency activities and the names of local government, regulatory agencies, institutions, and contractors that will provide support, mitigation, and relief in case of emergencies.  A copy of the contingency plan will be maintained at the facility and will be provided to local emergency service organizations.

2.0 	GENERAL INFORMATION

This contingency plan and emergency procedures are prepared for PFO with a mailing and site address at 10100 Rocket Boulevard, Orlando, Florida 32824.  The facility telephone number is (407) 859-4441.  The facility site is located in the southwest part of Orlando in the Regency Industrial Park, located approximately 3.5 miles west of the Orlando International Airport and about 1.5 miles to the southeast from the intersection of State Road 528 (Bee-Line Expressway) and the Florida Turnpike.  The PFO site may be accessed from north and south Orange Blossom Trail (OBT) through Taft-Vineland Road and the Central Florida Parkway, respectively, and through Taft-Vineland Road from Orange Avenue.  The closest road intersection on Rocket Boulevard from the facility is General Drive, which is located half a block away to the west.  The facility site, roads, and intersections mentioned above are shown in a map included in Figure II.A.4.b.-l.

The facility stores hazardous wastes in containers; and is permitted to treat hazardous waste and wastewaters in tanks.  Hazardous wastes received at PFO are generated by manufacturing and service industries.  The hazardous wastes are transported to the facility in containers or tank trucks.  Hazardous wastes that have adequate heating value are removed from inbound containers, blended for supplemental fuel, stored in tanks, and shipped off-site for energy recovery.  Acidic wastewater is neutralized, and contaminants are removed.  Wastewaters contaminated with hazardous organic and inorganic constituents are treated to remove the contaminating constituents.  Wastewater is stored in tanks after treatment prior to shipment to non-hazardous facilities.  The remaining portion of the wastes received at PFO that are not managed in any of the processes described above are either consolidated in bulk containers or shipped out in the same container in which they were received by the facility.

3.0 	EMERGENCY SERVICE ORGANIZATIONS

Table II.A.4.b.-1 lists the service type, name of the service organization, and telephone number for each organization that has been identified as a potential emergency service organization.  This list will be posted near telephones located in areas from which emergency calls are most likely to be made to provide callers with the information necessary to summon help in case of an incident.

The type of organizations that are most needed in case of an emergency are: Emergency Response (Hazardous Materials) Team, Fire Department, Hospital, and Sheriff’s Department. Figure II.A.4.b.-2 shows the locations of the organizations mentioned in the previous sentence that are closest to the PFO site.

The organizations listed in Table II.A.4.b.-1 will be provided with a copy of the contingency plan upon its approval by the Florida DEP.  These organizations will also be notified every time there is a change in:

- emergency coordinators or organizations as shown in Table II.A.4.b.-1.

2. 	waste type or location of waste types that pose an additional or different safety concern to the ones described in this plan.

3. 	structures, equipment, or operations that affect the way this plan is to be implemented.

4. 	structures, equipment, or operations that alter the level of hazard at the facility

5. 	emergency procedures contained in this plan that may affect the level of service to be rendered by these organizations.

This document will be amended to reflect any of the changes described above, and a copy of the amended document will be provided to those organizations.  This plan will also be amended when changes are necessary to improve response to emergencies.

Emergency organizations are expected to provide the following support during emergencies:

Hazardous Materials Emergency Response Team

The HAZMAT team will help mitigate hazards posed by hazardous materials that are out of control and help retrieve injured personnel from hazardous environments.  The unit that renders this type of service is based at Station #50, which is located near the intersection of Interstate 4 (I-4) and U.S. Highway 441 (OBT) about 7 miles north of the site at 1415 West 29 Street, Orlando (about 12 minutes from the facility).  This unit is known as Squad 1.  This organization will be provided with a copy of this contingency plan.

Fire Department

The Orange County Fire Department will respond to fires and other emergency incidents providing fire protection and rescue services.  The department operates units located in several stations near the PFO site.  These stations and their response capability are listed below.

Station #73: This unit is located in the town of Taft less than 2 miles northeast from the site at the intersection of Orange Avenue (State Road 527) and 1st Street, at 811 E. 1st Street, Orlando.  The response time for this unit is about 4 minutes.  This unit will be the first responder in the event of a fire.

Station #53: This unit is located just east of OBT about 2 miles northeast from the site, at 1270 La Quinta Drive, Orlando.  The response time is approximately 6 minutes.  The unit can provide medical support.

Station #51: This unit is located just west of OBT about 4.5 miles north from the site, at 1700 W. Oakridge, Orlando.  The unit’s response time is approximately 10 minutes.  The unit can provide a ladder truck in case of a fire.

A copy of the contingency plan for the Orange County Fire Department will be provided to the Deputy Chief, Operations at the Orange County Fire Rescue Division, 6590 Amory Court, Winter Park, Florida 32792, and to Orange County Office of the Fire Marshall, 109 East Church St., Orlando, Florida 33801 upon approval of the plan by the Florida DEP.

Hospital

Orlando Regional Health Services (ORHS) is capable of providing almost all emergency medical services that may be needed by injured personnel.  ORHS offers minor trauma services at the Sandlake unit located just west of I-4 and about 6 miles east of the site, at 9400 S. Turkey Lake Road, Orlando.  The time of travel is about 10 minutes from the facility.  ORHS offers major trauma services at the Orange Avenue unit (ORMC) located at about 8 miles north of the site at 1400 S. Orange Avenue, Orlando, Florida 32806.  The time of travel to this unit is about 14 minutes from the facility.  A copy of the contingency plan will be mailed to the ORMC Orange Avenue unit upon approval of this plan by the Florida DEP.

Sheriff's Department

The Orange County Sheriffs Office is available to direct traffic, handle crowds, and provide security during emergency situations.  The Sheriff will be provided a copy of this document at the Orange County Sheriff Office, P.O. Box 1440, Orlando, Florida 32802, upon its  approval by the Florida DEP.

Copies of the contingency plan, in accordance with statements shown above, will be provided to the emergency service organizations within 30 days after the permit is renewed.  Certified return receipt slips providing proof of mail and delivery of the documents will be kept with pertinent records at the facility.

Incidents of large magnitude may require the use of heavy equipment for containment, removal, and transportation of contaminated materials.  PFO operates another site nearby where an extensive transportation fleet made up of many tractors, roll-off boxes, and dump, tank, and van trailers is maintained.  The company also owns and operates a backhoe/front loader, and a number of forklifts, which will be used to provide fast response to a threat posed by a large release.  In the event that the equipment mentioned above is not available, PFO will seek the help of outside emergency response contractors to assist the facility during special emergency circumstances.

4.0	EMERGENCY COORDINATORS

In case of emergency, the following people would be in charge of emergency coordination and remedial action:

| NAME |  | HOME ADDRESS | PHONES |
| --- | --- | --- | --- |
| Raj Singh Primary Emergency Coordinator |  | 7676 Country Run Parkway Orlando, FL 32818 | Work: 407/859-4441 Home: 407/293-0598 |
|  |  |  | Cell: 407/399-6158 |
| Mike Avery Alternate Emergency Coordinator |  | 106 Alexandrea Avenue Minneloa, FL 34755 | Work:: 407/859-4441 Home: 352/394-1087 Cell: 321/230-4168 |

If an emergency situation develops at the facility, the discoverer should contact an emergency coordinator listed above.  Raj Singh, the primary emergency coordinator, should be contacted first.  If he is not available, Mr. Avery, the alternate emergency coordinator, should be called.

The primary emergency coordinator and his alternate have the authority to commit all resources of the company in the event of an emergency.

5.0 	AREAS AND MATERIAL PRESENTING POTENTIAL HAZARDS

The facility has several areas that present a potential hazard because of the materials that are stored or processed at those locations.  The degree of hazard present in these areas is based on the material types, the quantities managed, and the level of handling such materials.  These areas are the Container Storage Unit, the Waste Fuel Removal and Blending Unit, the Waste Fuel Tank Storage Unit, the Wastewater Tank Storage Unit, the Wastewater Treatment Unit, and the Consolidation Areas.  Figure II.A.4.b.-3 contains a layout of the PFO facility showing the areas listed above.  The portion of the facility that includes the areas mentioned above is considered the "active portion of the facility".  This section of the plan describes each area in detail, the operations conducted in each area, the materials handled, and where each type of material is stored or processed.

5.1 	Container Storage Unit

This area receives hazardous waste in drums that are stored on pallets.  The pallets are, at the most, double-stacked, with each pallet holding up to four – 55 gallon drums.  The pallets are placed in rows, as depicted in Figure II.A.4.b.-4.  Every row is identified with a sign showing the hazard class(es) of compatible wastes stored in the row.  The compatibility of different wastes within a cell is determined by a compatibility system established by the Department of Transportation (DOT).

The reason for using the DOT compatibility system is to prevent two incompatible materials from coming in contact with each other and generating a reaction, which could result in fire, explosion, or generation of toxic gases.  EPA hazardous waste codes are assigned based on the hazardous characteristics exhibited by the material.  These characteristics may be ignitability, corrosivity, reactivity, or toxicity.  A DOT hazard class is a number that indicates the category that has been assigned to a material based on the type of hazard it presents.  Table II.A.4.b.-2 contains the Segregation Table obtained from DOT.  It has been modified to delete hazard classes that PFO is not permitted to manage at the facility (1.1 through 1.6 - explosives, 6.2 - infectious substances, and 7 - radioactives)

The next table, labeled Table II.A.4.b.-3, lists the hazardous wastes stored in the container unit by waste description, EPA hazardous waste code, chemical abstracts service (CAS) registry number, and DOT hazard class.  This table is helpful in identifying the waste material because it shows the description and the CAS number, which can be used to find information about the material in chemical dictionaries, Material Safety Data Sheets (MSDSs), or other chemical information sources.  This table identifies unaltered waste materials based on the assigned hazardous waste codes.  Waste material properties and characteristics may be changed by the generation process or other conditions.  DOT hazard classes shown on containers that are stored in this unit are based on the actual properties and characteristics exhibited by the waste materials in the containers, in accordance with an evaluation of the waste completed before the waste was received by the facility.  The containers in this unit are placed in cells with the hazard classes displayed on the container and each cell.  The purpose of the segregation system instituted by PFO is to indicate to operators where to place specific waste containers within the unit and to provide emergency responders with an easy and quick way to identify hazards present within the unit.

Figure II.A.4.b.-4 shows the container storage unit, with locations of each row of pallets.  Signs showing the corresponding hazard classes for wastes currently stored in every cell will be posted on cell walls at locations clearly visible for first responders.

5.2 	Waste Fuel Removal and Blending Process

This process is located in a building adjacent to the west half section of the north wall of the container storage unit.  The west section of the north wall is made of brick.  The east half of the north wall is made of sheet metal to meet fire code requirements applicable to operations that were conducted in the process building in the past.  The east half section of the wall is not aligned with the west half, but is shifted about three feet, parallel and to the north of the west half.  Drums stored in the container storage unit are transferred to the removal and blending area through an opening made in the three-foot transverse wall section created by the shift of alignment between the halves of the unit's north wall.  The drums are placed on a conveyor on the container storage unit side.  This conveyor runs through the opening and takes the drums to liquid and solid removal stations.  The floor surface of the container storage unit has an elevation about four feet higher than the floor surface of the fuel process area.  This allows the conveyor to be sloped toward the fuel process area and the drums to run by gravity on the conveyor to the removal stations.  The removal stations are where liquid is removed from the drums, and the drums are opened and tilted over a trough for the removal of solids.  The removed waste is discharged into a blending tank where the waste's particle size is reduced, dispersed, and homogenized in a liquid medium.  A layout of the process is shown in Figure II.A.4.b.-5.

5.3 	Waste Fuel Tank Storage Unit

This unit is located to the west of the buildings housing the container storage unit and the waste fuel process described above.  The waste fuel storage unit is separated from the two buildings by a ramp used by forklifts to get from the container storage unit to the parking area.  Figure II.A.4.b.-6 contains a layout of this unit.  This tank farm holds a maximum volume of 60,000 gallons (four 15,000-gallon tanks) of ignitable liquid material produced by the removal and blending process described above.  Blended waste fuel is pumped into the tanks from the removal and blending process through a piping system and is then pumped from the storage tanks through pipes and hoses into tank trailers for shipment to energy recovery facilities.  The location where the tankers are loaded is an area that runs outside along the west side of the container loading/unloading dock and the tank farm.  The tank farm is contained in an area surrounded by walls about 4 feet high, which provide secondary containment for the control of spills.

5.4 	Wastewater Tank Storage Unit

This unit is located adjacent and to the north of the waste fuel tank storage unit.  The tank farm consists of four 10,000- and two 8,000-gallon tanks in an area provided with a secondary containment system.  A layout of the tank farm is shown in Figure II.A.4.b.-7.  Two of the tanks store acidic liquid materials that have a pH lower than 2.  All of the tanks in this area contain liquid materials that may be contaminated with organic and inorganic constituents.  The acidic material is very corrosive and should not be handled without appropriate personal protective equipment.

5.5 	Wastewater Treatment Process

This process equipment is located outside along the east side of the building that houses the waste fuel removal and blending process and at the north end of the wastewater tank storage unit.  The treatment equipment consists of two reactors for the neutralization of the acid liquids and precipitation of inorganic constituents, a filter press, ion exchange towers, and organic removal equipment.  Figure II.A.4.b.-7 contains a layout of this equipment.  The organic removal equipment consists of an air stripper and a carbon absorption unit, which, together with the filter press and the ion exchange towers, are located just outside the north end of the wastewater tank storage unit.  The neutralization/precipitation operation is a batch-type process that has a variable treatment time period.  The treatment period depends on the characteristics and composition of the wastewater being fed to the process.  However, the time to process any batch is not expected to last longer than a regular work-shift.  The other components - the filter press, the ion exchange towers, and organic removal equipment - comprise a serial process that treats wastewaters from the neutralization/precipitation operation.

5.6 	Consolidation Areas

This operation consists of taking waste material from inbound containers and placing it into another outbound container that holds a similar type of waste material.  Waste materials in both containers must be of similar type to meet acceptance criteria of off-site facilities.  Consolidation may occur from small containers holding as little as a few ounces to containers as large as a dump trailer.  Consolidation operations take place in an area located in the north half of the building that houses the waste fuel removal and blending process and just outside the north wall of the building.  A row of booths has been built along the internal side of the building's north wall for consolidation operations.  Waste managed in this area is transferred from the container storage unit with forklifts or on the conveyor in quantities that are estimated not to exceed the amount of waste that can be consolidated in one work-shift.  A plan view of the consolidation area inside the building is shown in Figure II.A.4.b.-5.  Another consolidation area identified as the Consolidation Pad is a bermed space located just outside the north end of the wastewater tank storage unit, next to the organic removal equipment.  This space is used primarily to consolidate corrosive liquids in 55-gallon or smaller containers into tote tanks or the storage tanks located in the adjacent tank farm.  This consolidation pad may be used if the other consolidation area located inside the building cannot be used.  In addition, solid materials may be bulked in a roll-off or other bulk container placed just outside the north wall.  These areas are shown in Figure II.A.4.b.-8.

6.0 	IMPLEMENTATION OF CONTINGENCY PLAN

The decision to implement the contingency plan depends upon whether or not an imminent or actual incident could potentially threaten human health and safety or the environment.  This plan provides specific guidelines for activating the emergency procedures in the contingency plan.  Three factors will be evaluated: potential hazards of confined spills, spills affecting incompatible wastes, and uncontrolled spills.  If a spill inside a secondary containment poses a threat in the form of fire or explosion or creates a health problem, the contingency plan will be activated.  Emergency procedures in the contingency plan will be implemented when spilled material comes in contact with incompatible wastes and there is a potential of a reaction that may result in fire, an explosion, or generation of poisonous or flammable gases.  Uncontrolled spills that have the potential or have resulted in releases to the environment in magnitudes that equal or exceed reportable quantities in the 40 CFR 302.4 will also require the implementation of the contingency plan.  Releases are defined in the 40 CFR 302.3.  The Florida DEP will be notified of incidents at the facility requiring the implementation of the contingency plan or when the size of the release into the environment equals or exceeds the reportable quantities.  All spills will be documented in inspection records.  The next sections will provide guidance to the emergency coordinators in making decisions by providing explicit instructions to be carried out in the event of an emergency.

7.0 	EMERGENCY PROCEDURES

Upon being notified by facility personnel or government officials of a hazardous waste release, the Emergency Coordinator will -

1. 	Immediately identify the character, exact source, amount, and real extent of any released materials via observation, review of facility records, or chemical analysis, if necessary.

2. 	Call in any extra personnel needed to complete the initial evaluation of the situation.

3. 	Concurrently assess possible hazards to human health or the environment via the above determinations.

4. 	Notify key support and key management personnel.

5. 	Seek assistance from the Orange County Sheriffs Department, Fire Department and the Florida DEP Central District Hazardous Waste Section, as needed.

6. 	Notify either the government official designated as the on-scene coordinator for that geographical area or the National Response Center (using their 24-hour toll free number 800/424-8802).  The report must include:

(i) 	Name and telephone number of reporter

(ii) 	Name and address of facility

(iii) 	Time and type of incident (e.g., release, fire)

(iv) 	Name and quantity of material(s) involved, to the extent known

(v) 	The extent of injuries, if any, and

(vi) 	The possible hazards to human health, or the environment, outside the facility

7. 	Notify the Florida DEP’s 24-hour warning point at 1-800-320-0519 if human health or the environment may be threatened outside the facility.  The determination for the need of notification shall be made with the knowledge of the above assessment of actual conditions.

8. 	Take all reasonable measures necessary during an emergency to ensure that fires, explosions, and releases do not occur, recur, or spread to the other hazardous waste at the facility.  All operations shall stop, containers shall be removed and isolated, containment systems shall be inspected, and emergency equipment shall be utilized.

9. 	Provide for treating, storing, or disposing of recovered waste, contaminated soil, or any other material that results from a release, fire, or explosion at the facility.

10. 	Ensure that no waste that may be incompatible with the released material is treated, stored, or disposed of until cleanup procedures are completed.

11. 	Ensure that all emergency equipment is cleaned and fit for its intended use before operations are resumed.  Used fire extinguishers shall be replaced, and other equipment shall be inspected as necessary.

12. 	Notify the Secretary of the Florida DEP, and appropriate state and local authorities that the cleanup has been completed; the released material has been treated, stored, or disposed of; and emergency equipment has been cleaned and fit for use before operations are resumed in the facility.

13. 	Submit a written report on the incident to FDEP and USEPA Region IV within 15 days after the incident and identify such incidents in the facility operating record. The report will include:

(i) 	Name, address, and telephone number of the owner or operator

(ii) 	Name, address, and telephone number of the facility

(iii) 	Date, time, and type of incident (e.g., fire, explosion)

(iv) 	Name and quantity of material(s) involved

(v) 	The extent of injuries, if any

(vi) 	An assessment of actual or potential hazards to human health or the environment, where this is applicable, and

- Estimated quantity and disposition of recovered material that resulted from the incident

FDEP and USEPA offices who must receive the above report are as follows:

a.	One (1) copy to:		Hazardous Waste Supervisor

Florida Dept. of Environmental Protection

Suite 232

3319 Maguire Blvd.

Orlando, FL 32803-3767

b.	Two(2) copies to:		Environmental Administrator

Hazardous Waste Regulation Section

Bureau of Solid & Hazardous Waste									Florida Dept. of Environmental Protection

M.S. 4560

2600 Blair Stone Road

Tallahassee, FL  32399-2400

c.	One (1) copy to:		Chief, RCRA Programs Branch

U. S. Environmental Protection Agency

Region IV

Sam Nunn Atlanta Federal Center

61 Forsyth Street, S.W.

Atlanta, GA  30303-3104

7.1 	Responses to Fires, Explosion, and Releases

The previous section was designed to provide general guidance for making decisions and to be used as a check-list during the implementation of the contingency plan.  This section deals with the effect that the type and amount of waste materials managed in the operation areas may have on the occurrence and development of emergency incidents at the facility.  It also indicates features and equipment found or available in the area that may help mitigate such incidents.  The two types of incidents discussed here are only fire and waste material release.  Explosions will result either in a fire or a release, which are the incidents addressed in this plan.

7.1.1 	Container Storage Unit

This area is considered the area within the active portion of the facility that presents the highest level of potential hazard because of the quantity and types of waste materials present in the area.  The largest potential danger in this unit is fire due to the large amount of ignitable material that may be stored in it.  Containers that arrive at this unit are opened only for sampling, after which they are placed in a storage cell in accordance with the DOT hazard class displayed on the container.  As explained in section 5.1 above, the waste materials are segregated into cells having separate secondary containments. Cell segregation and careful management of container placement shall prevent commingling of incompatible wastes.  Only incipient fires will be fought in this area by using any of the 20-pound or the 150-pound fire extinguishers located inside or outside near the entrances to the unit.  If the fire is not put out within a few seconds of the fire's initial stage, the fire alarm will be activated as the first step in the implementation of the contingency plan.  This storage unit is equipped with an automatic fire sprinkler system that covers the unit’s entire area.

Every cell in this unit is provided with secondary containment capable of containing more than 10% of the maximum storage volume permitted for the cell.  If the secondary containment capacity of a cell is exceeded, overflow will spill into another cell, from which, when exceeded, overflow will spill into another cell, and so on.  The only way a spill may be released outside the unit is if the spill becomes of such magnitude that it exceeds all the internal cells' secondary containment volumes, and the capacity of the berm that surrounds the entire unit.  The berms and walls that surround the entire unit are higher than the berms that provide containment for the internal cells.  Therefore, a release to areas outside the container storage unit is unlikely.

Spi1ls confined to the cell where the spill occurs should not present a hazard to human health or the environment as long as the spill is cleaned up within a reasonable period of time in accordance with proper safety procedures.  Such spills will not activate the implementation of the emergency procedures in this contingency plan.

Spills that exceed the cells' secondary containment volume will not activate the implementation of the contingency plan as long as the spill only affects cells that store compatible waste materials.  Spills will be confined to the smallest possible area using sorbent booms and oil dry.  Standing liquid pools will be collected with air driven pumps and/or sorbent material.  A spill from only one cell that affects another cell, which stores waste that is not compatible with the spilled material, will activate the implementation of the contingency plan, and the spill will be collected immediately with great care.  The spilled material will be transferred to containers and identified from information obtained in the waste characterization process.  Spills where two or more waste streams become commingled may require testing of the release for characterization depending on whether spilled waste streams were identified and on whether the collected material may be substantially different from the spilled waste streams.  Spills that result in releases outside the unit will require full implementation of the contingency plan.  Waste spilled outside the unit will be contained in a series of berms and curbs in the parking lot.  If these berms and curbs are overrun, they will spill into the stormwater pond.  Releases into the soil will require removal of contaminated soil and verification of decontamination through sampling and testing of surrounding soils.  All collected wastes from spills will be properly disposed of by permitted methods.

7.1.2 	Waste Fuel Removal and Blending Process

This process manages ignitable materials.  The number of drums handled in this area at any time should not exceed 30 drums or the equivalent of 1,650 gallons of waste, which, when added to the 700 gallons of waste in the blending tank, results in a maximum volume that is managed in this area of 2,350 gallons.  This volume seems small when compared to the volume managed in the container storage unit (65,120 gallons), which indicates that the hazard present due to the quantity of waste handled in this area is not large.  However, the materials managed in this area are ignitable, and the level of active handling is larger than in other areas, which increases the possibility of fire.  The point in this process that has the highest danger of fire is the waste removal station because waste is exposed to combustion factors in the form of air (oxygen) and spark generation.  The concern about sparks in this point of the process is due to the use of tools and the contact of the waste with moving equipment parts.  Tools and moving equipment parts are to be made of non-sparking materials or must remain submerged in waste liquid.  To respond to fires in a quick and effective manner, nozzles have been installed at each station that are capable of spraying fire-suppressing foam at a high rate of delivery.  The activation of the fire-fighting foam system at the stations is manual from locations inside and outside the station.  The blending tank presents a lesser degree of fire potential because it is totally enclosed, except for an opening on the side where the removal station discharges waste into the tank, and because moving parts inside the tank are constantly submerged in waste liquid.  To prevent fires from spreading to the tank, another fire-suppressing, foam-spraying nozzle has been installed at the center above the tank.  Several 20-pound and a 150-pound fire extinguisher are located in this are for use in containing and subdueing small and incipient fires in this area.  If the fire is not extinguished during the first few seconds of its initial stage, the fire alarm will be activated and the contingency plan will be implemented.  The entire building area is covered with an automatic fire sprinkler system.

The removal and blending process is confined to a building whose internal perimeter is surrounded with a 3-inch berm, which is capable of containing several times the maximum volume of wastes that may be managed in the process at any time.  Therefore, spills of any magnitude from this process will not have a chance to escape the building area.  Spills in this building will be confined to the smallest possible area with sorbent booms and oil dry.  Standing liquid pools will be collected using air-driven pumps and/or sorbent materials.

7.1.3 	Waste Fuel Tank Storage Unit

This unit stores the largest amount of ignitable liquids in the facility.  The storage tanks have a maximum volume of 60,000 gallons of blended waste fuel.  Due to the volume of dangerous materials managed in this tank farm and the fact that there is some active handling in this area, this unit presents a level of hazard that should be taken into consideration when responding to fire incidents at the facility.  The point that has the highest fire risk in this tank farm is the area where the wastes are pumped into the tank trailers for transport off-site.  Waste fuel may be exposed during the connection of hoses to the tank.  The tank truck loading area is the strip of parking lot that runs outside along the west walls of the container loading/unloading dock and tank farm; however, the pump and the high-pressure end of the loading hose are located within the confines of the tank farm.  Several 20-pound and a 150-pound fire extinguisher are strategically located nearby to fight the initial stages of a fire.

The waste fuel tank storage unit is surrounded by walls about 4 feet high to provide a secondary containment capable of containing a spill the size of any of the unit's four 15,000-gallon tanks.  A spill larger than that size will be ultimately contained in the stormwater pond.  Spills that may occur in the tanker loading area will be contained by berms and curbs built on the parking lot.  Spills inside and to the outside of the tank farm's secondary containment will be collected and decontaminated in the manner described in the section addressing the container storage unit.  Uncontrolled spills in the tank farms and in the tanker loading areas that have the potential of resulting, or have resulted, in releases exceeding the reportable quantities will require the implementation of the contingency plan.  There is little concern about the commingling of the incompatible spilled materials at these locations because waste materials handled are compatible.

7.1.4 	Wastewater Tank Storage Unit

This unit is located inside 2-foot high walls designed to contain spills larger than 10,000 gal1ons.  Such spills consist of highly acidic wastes and/or liquids contaminated with organic and inorganic constituents.  The materials presenting the greatest hazard are the acidic wastes because the corrosiveness can cause human injury and affect the integrity of any equipment, building, or structure with which it may come in contact.  In case of acid spills, personnel conducting the response need to wear appropriate personal protective equipment.  Equipment, tools, and containers used to collect acid spills should be made of corrosive-resistant materials.  The tank farm does not store other materials that are incompatible with acids; however, releases need to be collected as soon as possible to prevent damage to other tanks, pumps, and secondary containment structure.  Liquids contaminated with organic and inorganic constituents that are also stored in this unit do not present an immediate hazard to personnel dealing with emergency incidents, but do pose an environmental concern.  Acid releases outside the tank farm will be contained in berms and curbs built on the parking lot and finally in the stormwater pond.  Acids spilled inside and outside the tank farm will be contained and collected with absorbent booms, oil dry, and corrosive-resistant pumps.  Removal of organic and inorganic contaminants from soils affected by releases will require verification of decontamination by testing the surrounding soils.  There are no fire hazards present in this unit.  The same criteria used to implement the contingency plan in the waste fuel tank storage unit also applies to this unit, as well as to the tanker loading area used to transfer waste from this unit.

7.1.5 	Wastewater Treatment Process

This process is located inside a bermed area, which is capable of containing a spill the size of the maximum volume that may be managed in this area.  The materials handled in this process are the same that are stored in the wastewater tank storage unit.  Likewise, the containment, collection, and removal of releases will be conducted in the manner described for the tank storage unit.

7.1.6 	Consolidation Area

Operations conducted in this area involve more solids than liquids.  Liquids managed in this operation are materials that are pumped into the wastewater tanks after they have been received at the facility, certain types of acids that cannot be treated on site, caustics, labpacks, inorganic contaminants, and small quantities of materials that have hazardous properties, like oxidizers and combustible solids.  Materials are tested for compatibility before they are consolidated.  The consolidation area inside the building is equipped with an automatic fire sprinkler system and there are a number of 20-pound and 150-pound fire extinguishers either in the area or nearby.  The consolidation area is bermed to contain the largest quantity of wastes that may be managed in it.

8.0 	EMERGENCY EQUIPMENT

The facility is equipped with the adequate emergency equipment to respond to all kinds of emergency incidents.  The emergency equipment is placed in strategic locations where it can be reached quickly and safely in the event of an emergency.

All emergency equipment is dedicated to emergency situations and is not used for normal operations.  Use of the emergency equipment is not limited to events that require implementation of the Contingency Plan.  However, all emergency equipment will be cleaned and fit for use immediately after it has been used and will be placed in the locations indicated in this section of the plan.  To control access to cabinets and assure immediate identification of status, cabinets will be secured with a seal that is easy to break.  Only one person will be designated the keeper and replacer of the seals.  Weekly inspections will ensure that the emergency equipment is complete and ready to use.

Alarm switches are located in the administration building.  One alarm switch is located at each process area and storage unit.  These alarm switches, when operated, actuate an on-site audible signal, loud enough to assure the attention of anyone located on the premises.  The switch also automatically summons the help of the fire department.  Since the property is small in area and all active areas and units are open to the outside, a spoken call for help can be heard in all the active areas of the facility where several operators are working during working hours.  The location and capabilities of alarm switches and the small area of the facility make internal communication devices unnecessary for emergency situations.

A fire hydrant, located near the entrance to the facility, provides water in case of a fire.  A fire sprinkler system services the container storage unit and the waste removal and blending process area.  There is a phone next to the receptionist that works even during power outages.  Power outages will neither create an incident during normal operation processes nor affect response to emergency situations.

Figure II.A.4.b.-9 shows the location of the emergency equipment.  Table II.A.4.b.-4 lists the equipment stored in the cabinets and shown in the figure mentioned above.

9.0 	EVACUATION PLAN

All emergencies require prompt and deliberate action.  In the event of any major emergency, it will be necessary to follow an established set of procedures.  Such established procedures will be followed as closely as possible; however, in specific emergency situations, the Emergency Coordinator may deviate from the procedures to provide a more effective plan for bringing the situation under control.  The Emergency Coordinator is responsible for determining which emergency situations require plant evacuation.

Total plant evacuation is initiated only by the Emergency Coordinator.  A fire alarm system is installed with alarm boxes located at critical areas in the facility.  The fire alarms can also be used to summon aid in other emergency situations.  All employees are familiar with relevant alarm box locations.

In the event plant evacuation is called for by the Emergency Coordinator, the following actions will be taken:

a. 	The signal for plant evacuation will be activated.

b. 	No further entry of visitors, contractors, or trucks will be permitted.  All vehicle traffic within the plant will cease to allow safe exit of personnel and movement of emergency equipment.

c. 	ALL personnel, visitors, and contractors will immediately leave through the exit gate to gather at the designated rally point.

d. 	No persons shall remain or reenter the location, unless specifically authorized by the person or persons calling for the evacuation.  In allowing this, the person in charge assumes responsibility for those persons within the perimeter.  Those within the fenced area will normally only include fire brigade personnel or emergency teams.

e. 	ALL persons will be accounted for by their immediate supervisors.

f. 	The appointed rally point is located at Rocket Boulevard by the east gate.  Immediately upon exit, the highest ranking supervisor will compile a list of all personnel at the rally point.

g. 	Upon completion of the employee list, the supervisor in charge will hand-carry the list to the Emergency Coordinator.  All other personnel will remain at the gate area.

h. 	The names of plant personnel and/or other emergency team members involved in emergency response will be reported, in writing, to the front gate by designated response team personnel.

i. 	A final tally of personnel will be made by the Emergency Coordinator.

j. 	An attempt to find persons not accounted for will be made only if it does not involve endangering lives of others by reentry into emergency areas.

k. 	Reentry in the fenced area will be made only after clearance is given by the Emergency Coordinator.  At his or her direction, a signal or other notification will be given for reentry into the plant.

l. 	In all questions of accountability, immediate supervisors will be held responsible for those persons reporting to them.  Visitors will be the responsibility of those employees being visited.  Contractors are the responsibility of those persons administering the individual contracts.  Truck drivers are the responsibility of the warehouse supervisor or the area supervisor where the truck is loading/unloading.

m. 	Drills are held to practice all of these procedures and are treated with the same seriousness as an actual emergency.

Figure II.A.4.b.-l0 shows routes employees and other persons at the facility at the time of an emergency will take when an evacuation is ordered.

Table II.A.4.b.-1

Emergency Contacts, Service Organizations, and Phones

PERMA-FIX OF ORLANDO, INC. EMERGENCY COORDINATORS

Raj Singh, Operations Manager				Work 407/859-4441

Primary Emergency Coordinator				Home 407/293-0598

Cell 407/399-6158

Mike Avery, Transportation Manager			Work 407/859-4441

Alternate Emergency Coordinator				Home 352/394-1087

Cell 321/230-4168

## EMERGENCY AGENCIES / OUTSIDE CONTRACTORS

WHO MAY BE INVOLVED IN CASE OF AN EMERGENCY

INJURY

Ambulance -						911

Orlando Regional Medical Center -			407/841-5111

Poison Control Center -				407/841-5222

FIRE

#### Orange County Fire Dept. -				911

EXPLOSION

Orange County Sherriff -				911

SECURITY / FIRE ALARMS

Wayne Automatic Fire Sprinklers - 			407/656-3030

HAZARDOUS MATERIALS SPILL OR RELEASE

Orange County Fire Dept. & Hazmat Team -		911

Orange County Environmental Protection -		407/836-1400

Florida State Warning Point -				850/413-9911 or 800/320-0519

Natural Response Center/DOT Spills -		800/424-8802

Florida DEP Central District Office - 		407/894-7555

#### Clean Harbors Emergency Response	-		800/645-8265

NATURAL DISASTER

Orange County Office of Emergency Management 	407/836-9140

FLOODING

Orange County Storm Water Management -		407/836-7946

ALL OF THE ABOVE

Orange County Office of Emergency Mgt. -		407/836-9140

Table II.A.4.b.-2

Segregation Table for Hazardous Materials

| Class or Division | 2.1 | 2.2 | 2.3 gas Zone A | 2.3 gas Zone B | 3 | 4.1 | 4.2 | 4.3 | 5.1 | 5.2 | 6.1 liquids PG I Zone A | 8 liquids only | 9 H.S. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Flammable gases 2.1 |  |  | X | O |  |  |  |  |  |  | O | O |  |
| Non-toxic, non-flammable gases 2.2 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Poisonous gas Zone A 2.3 | X |  |  |  | X | X | X | X | X | X |  | X |  |
| Poisonous gas Zone B 2.3 | O |  |  |  | O | O | O | O | O | O |  | O |  |
| Flammable liquids 3. |  |  | X | O |  |  |  |  | O |  | X |  |  |
| Flammable solids 4.1 |  |  | X | O |  |  |  |  |  |  | X | O |  |
| Spontaneously combustible materials 4.2 |  |  | X | O |  |  |  |  |  |  | X | X |  |
| Dangerous when wet materials 4.3 |  |  | X | O |  |  |  |  |  |  | X | O |  |
| Oxidizers 5.1 |  |  | X | O | O |  |  |  |  |  | X | O |  |
| Organic peroxides 5.2 |  |  | X | O |  |  |  |  |  |  | X | O |  |
| Poisonous liquids PG I Zone A 6.1 | O |  |  |  | X | X | X | X | X | X |  | X |  |
| Corrosive liquids 8 |  |  | X | O |  | O | X | O | O | O | X |  |  |
| Hazardous substances 9 |  |  |  |  |  |  |  |  |  |  |  |  |  |

Note:  Codes X and O indicate prohibitions and restrictions as noted below.

(	An “X” in the table indicates that these materials may not be loaded, transported, or stored together.

(	An “O” indicates that these materials may not be transported or stored together unless separated in such a way that, in the event or leakage from packages under normal transportation conditions, the hazardous materials could not commingle.  Regardless of the methods of separation employed, Class 8 (corrosive) liquid materials may not be loaded above Class 4 (flammable solid) materials or Class 5 (oxidizing) materials.

(	Cyanides or cyanide mixtures must not be loaded or stored with acids or acidic materials.  The reaction of cyanides with acids releases deadly hydrogen cyanide gas.

(	When the 172.101 Table or 49 CFR 172.402 requires a package to bear a subsidiary hazard label, segregation appropriate to the subsidiary hazard must be applied when that segregation is more restrictive than that required by the primary hazard.  However, hazardous materials of the same class may be stored together without regard to segregation required for any secondary hazard if the materials are not capable of reacting dangerously with each other and causing combustion or dangerous evolution of heat; evolution of flammable, poisonous, or asphyxiant gases; or formation of corrosive or unstable materials.

Table II.A.4.b.-3

Waste Stored at Perma-Fix of Orlando, Inc.

| Waste Description | Hazardous Waste Code | CAS Registry Number | Hazard Class |
| --- | --- | --- | --- |
| Ignitable Liquid | D001 | N/A | 3 |
| Corrosive (Acid, Caustic) | D002 | N/A | 8 |
| Reactive Liquids & Solids | D003 | N/A | N/A |
| Arsenic | D004 | 7440-38-2 | 6.1 |
| Barium | D005 | 7440-39-3 | 4.3 |
| Cadmium | D006 | 7440-43-9 | 6.1 |
| Chromium (Haz. Substance) | D007 | 7440-47-3 | 9 |
| Lead | D008 | 7439-92-1 | 6.1 |
| Mercury | D009 | 7439-97-6 | 8 |
| Selenium (Powder) | D010 | 7782-49-2 | 6.1 |
| Silver (Haz. Substance) | D011 | 7440-22-4 | 9 |
| Endrin (Haz. Substance) | D012 | 72-20-8 | 9 |
| Lindane (Haz. Substance) | D013 | 58-89-9 | 9 |
| Methoxychlor (Haz. Substance) | D014 | 72-43-5 | 9 |
| Toxaphene (Haz. Substance) | D015 | 8001-35-2 | 9 |
| 2,4-D (Acid – Haz. Substance) | D016 | 94-75-7 | 9 |
| 2,4,5-TP (Silvex) (Haz. Substance) | D017 | 93-72-1 | 9 |
| Benzene | D018 | 71-43-2 | 3 |
| Carbon Tetrachloride | D019 | 56-23-5 | 6.1 |
| Chlordane (Haz. Substance) | D020 | 57-74-9 | 9 |
| Chlorobenzene | D021 | 108-90-7 | 3 |
| Chloroform | D022 | 67-66-3 | 6.1 |
| O-Cresol | D023 | 95-48-7 | 6.1 |
| M-Cresol | D024 | 108-39-4 | 6.1 |
| P-Cresol | D025 | 106-44-5 | 6.1 |
| Cresol | D026 | 1319-77-3 | 6.1 |
| 1,4-Dichlorobenzene | D027 | 106-46-7 | 6.1 |
| 1,2-Dichloroethane (Ethylene Dichloride) | D028 | 109-06-2 | 3 |
| 1,1-Dichloroethylene (Vinylidene Chloride) | D029 | 75-35-4 | 3 |
| 2,4-Dinitrotoluene | D030 | 121-14-2 | 6.1 |
| Heptachlor (Haz. Substance) | D031 | 76-44-8 | 9 |
| Hexachlorobenzene | D032 | 118-74-1 | 6.1 |
| Hexachlorobutadiene | D033 | 87-68-3 | 6.1 |
| Hexachloroethane (Haz. Substance) | D034 | 67-72-1 | 9 |
| Methyl Ethyl Ketone (Ethyl Methyl Ketone) | D035 | 78-93-3 | 3 |
| Nitrobenzene | D036 | 98-95-3 | 6.1 |
| Pentachlorophenol (Haz. Substance) | D037 | 87-86-5 | 9 |
| Pyridine | D038 | 110-86-1 | 3 |
| Tetrachloroethylene | D039 | 127-18-4 | 6.1 |
| Trichloroethylene | D040 | 79-01-6 | 6.1 |
| 2,4,5-Trichlorophenol (Haz. Substance) | D041 | 95-95-4 | 9 |
| 2,4,6-Trichlorophenol (Haz. Substance) | D042 | 88-06-2 | 9 |
| Vinyl Chloride | D043 | 110-86-1 | 2.1 |
| Spent Halogenated Solvents (Haz. Substance) | F001 | N/A | 9 |
| Spent Halogenated Solvents (Haz. Substance) | F002 | N/A | 9 |
| Spent Non-Halogenated Solvents (Haz. Substance) | F003 | N/A | 9 |
| Spent Non-Halogenated Solvents (Haz. Substance) | F004 | N/A | 9 |
| Spent Non-Halogenated Solvents (Haz. Substance) | F005 | N/A | 9 |
| Electroplating Sludges (Haz. Substance) | F006 | N/A | 9 |
| Spent Cyanide Plating Solvents (Haz. Substance) | F007 | N/A | 9 |
| Plating Bath Residues (Haz. Substance) | F008 | N/A | 9 |
| Spent Stripping Solutions (Haz. Substance) | F009 | N/A | 9 |
| Quenching Bath Residues (Haz. Substance) | F010 | N/A | 9 |
| Spent Cyanide Solution (Haz. Substance) | F011 | N/A | 9 |
| Quench Wastewater Sludge (Haz. Substance) | F012 | N/A | 9 |
| Wastewater Treatment Sludge (Haz. Substance) | F019 | N/A | 9 |
| Chlorophenolic Residuals (Haz. Substance) | F032 | N/A | 9 |
| Creosote Residuals (Haz. Substance) | F034 | N/A | 9 |
| Arsenic/Chromium Residuals (Haz. Substance) | F035 | N/A | 9 |
| Petroleum Refinery Primary Sludge (Haz. Substance) | F037 | N/A | 9 |
| Petroleum Refinery Secondary Sludge (Haz. Subs.) | F038 | N/A | 9 |
| Leachate from Wastes (Haz. Substance) | F039 | N/A | 9 |
| Dissolved Air Float (Haz. Substance) | K048 | N/A | 9 |
| Stop Oil Emulsion Solids (Haz. Substance) | K049 | N/A | 9 |
| Heat Exchanger Sludge (Haz. Substance) | K050 | N/A | 9 |
| API Separator Sludge (Haz. Substance) | K051 | N/A | 9 |
| Petroleum Tank Bottoms (Haz. Substance) | K052 | N/A | 9 |
| Emission Control Dust/Sludge (Haz. Substance) | K061 | N/A | 9 |
| Spent Pickle Liquor (Haz. Substance) | K062 | N/A | 9 |
| Solvent Washes & Sludge (Haz. Substance) | K086 | N/A | 9 |
| Organic Wastes | K156 | N/A | 9 |
| Wastewaters | K157 | N/A | 9 |
| Baghouse Dusts & Filter Separator Solids | K158 | N/A | 9 |
| Organics from Treatment of Thiocarbamate Wastes | K159 | N/A | 9 |
| Solids | K160 | N/A | 9 |
| Purification Solids | K161 | N/A | 9 |
| Warfarin & Salts when >.03% (Haz. Substance) | P001 | 81-81-2 | 9 |
| Acetamide, N-(Aminothioximethyl) (Haz. Substance) | P002 | 591-08-2 | 9 |
| Acrolein | P003 | 107-02-8 | 6.1 |
| Aldrin | P004 | 309-00-2 | 6.1 |
| Allyl Alcohol | P005 | 107-18-6 | 6.1 |
| Aluminum Phosphide | P006 | 20859-73-8 | 4.3, 6.1 |
| 5-(Aminomethyl)-3-Isoxazolol (Haz. Substance) | P007 | 2763-96-4 | 9 |
| 4-Aminopyridine | P008 | 504-24-5 | 6.1 |
| Arsenic Acid (H3AsO4) | P010 | 131-74-8 | 6.1 |
| Arsenic Oxide (As2O5) | P011 | 1303-28-2 | 6.1 |
| Arsenic Oxide (As2O3) | P012 | 1327-53-3 | 6.1 |
| Barium Cyanide | P013 | 542-62-1 | 6.1 |
| Benzenethiol (Phenyl Mercaptan) | P014 | 108-98-5 | 6.1 |
| Beryllium (Powder) | P015 | 7440-41-7 | 6.1 |
| Dichloromethylether ((Haz. Substance) | P016 | 542-88-1 | 9 |
| Bromoacetone | P017 | 598-31-2 | 6.1 |
| Brucine | P018 | 357-57-3 | 6.1 |
| Dinoseb | P020 | 88-85-7 | 9 |
| Calcium Cyanide | P021 | 592-01-8 | 6.1 |
| Carbon Disulfide | P022 | 75-15-0 | 3, 6.1 |
| Acetaldehyde, Chloro- (Haz. Substance) | P023 | 107-20-0 | 9 |
| Benzenamine, 4-Chloro- (Haz. Substance) | P024 | 106-47-8 | 9 |
| 1-(o-Chlorophenyl)thiourea (Haz. Substance) | P026 | 5344-82-1 | 9 |
| 3-Chloropropionitrile (Haz. Substance) | P027 | 542-76-7 | 9 |
| Benzene, Chloromethyl (Benzyl Chloride) | P028 | 100-44-7 | 6.1 |
| Copper Cyanide | P029 | 544-92-3 | 6.1 |
| Cyanides (Solutions & Inorganics) | P030 | 57-12-5 | 6.1 |
| 2-Cyclohexyl-4,6-dinitrophenol (Haz. Substance) | P034 | 131-89-5 | 9 |
| Arsonous Dichloride, Phenyl (Haz. Substance) | P036 | 696-28-6 | 9 |
| Dieldrin | P037 | 60-57-1 | 6.1 |
| Arsine, Diethyl- (Haz. Substance) | P038 | 692-42-2 | 9 |
| Disulfoton (Haz. Substance) | P039 | 298-04-4 | 9 |
| 0,0-Diethyl 0-pyrazinyl Phosphorothioate (Haz. Subs.) | P040 | 297-97-2 | 9 |
| Diethyl-p-nitrophenyl Phosphate (Haz. Substance) | P041 | 311-45-5 | 9 |
| Epinephrine | P042 | 329-65-7 | 6.1 |
| Diisopropylfluorophosphate (Haz. Substance) | P043 | 55-91-4 | 9 |
| Dimethoate (Haz. Substance) | P044 | 60-51-5 | 9 |
| Thiofanox (Haz. Substance) | P045 | 39196-18-4 | 9 |
| Benzeneethanamine, alpha, alpha-dimethyl (Haz. Subs.) | P046 | 122-09-8 | 9 |
| 4,6-Dinitro-o-cresol & Salts (Solid or Solutions) | P047 | 534-52-1 | 6.1 |
| 2,4-Dinitrophenol (Haz. Substance) | P048 | 51-28-5 | 9 |
| Dithiobiuret (Haz. Substance) | P049 | 541-53-7 | 9 |
| Endosulfan (Haz. Substance) | P050 | 115-29-7 | 9 |
| Endrin (Haz. Substance) | P051 | 72-20-8 | 9 |
| Aziridine (Ethyleneimine) | P054 | 151-56-4 | 6.1 |
| Acetamide, 2-Fluoro- (Haz. Substance) | P057 | 640-19-7 | 9 |
| Acetic Acid, Fluoro-, Sodium Salt (Haz. Substance) | P058 | 62-74-8 | 9 |
| Heptachlor (Haz. Substance) | P059 | 76-44-8 | 9 |
| Isodrin (Haz. Substance) | P060 | 465-73-6 | 9 |
| Hexaethyl Tetraphosphate | P062 | 757-58-4 | 6.1 |
| Hydrogen Cyanide | P063 | 74-90-8 | 6.1, 3 |
| Methyl Isocyanate | P064 | 624-83-9 | 6.1 |
| Methomyl (Haz. Substance) | P066 | 16752-77-5 | 9 |
| Aziridine, 2-methyl | P067 | 75-55-8 | 3 |
| Methyl Hydrazine (Haz. Substance) | P068 | 60-34-4 | 9 |
| 2-Methyllactonitrile | P069 | 75-86-5 | 6.1 |
| Aldicarb (Haz. Substance) | P070 | 116-06-3 | 9 |
| Methyl Parathion | P071 | 298-00-0 | 6.1 |
| alpha-Naphthylthiourea | P072 | 86-88-4 | 6.1 |
| Nickel Carbonyl | P073 | 13463-39-3 | 6.1, 3 |
| Nickel Cyanide | P074 | 577-19-7 | 6.1 |
| Nicotine & Salts | P075 | 54-11-5 | 6.1 |
| Benzenamine, 4-Nitro- (p-Nitroaniline) | P077 | 100-01-6 | 6.1 |
| N-Nitrosodimethylamine (Haz. Substance) | P082 | 62-75-9 | 9 |
| N-Nitrosomethylvinylamine (Haz. Substance) | P084 | 4549-40-0 | 9 |
| Octamethylpryophosphoramide (Haz. Substance) | P085 | 152-16-9 | 9 |
| Osmium Tetroxide | P087 | 20816-12-0 | 6.1 |
| Endothall (Haz. Substance) | P088 | 145-73-3 | 9 |
| Parathion | P089 | 56-38-2 | 6.1 |
| Phenylmercury Acetate | P092 | 62-38-4 | 6.1 |
| Phenylthiourea (Haz. Substance) | P093 | 103-85-5 | 9 |
| Phorate (Haz. Substance) | P094 | 298-02-2 | 9 |
| Famphur (Haz. Substance) | P097 | 52-85-7 | 9 |
| Potassium Cyanide | P098 | 151-50-8 | 6.1 |
| Potassium Silver Cyanide (Haz. Substance) | P099 | 506-61-6 | 9 |
| Ethyl Cyanide (Haz. Substance) | P101 | 107-12-0 | 9 |
| Propargyl Alcohol | P012 | 107-19-7 | 3 |
| Selenourea (Haz. Substance) | P103 | 630-10-4 | 9 |
| Silver Cyanide | P104 | 506-64-9 | 6.1 |
| Sodium Azide | P105 | 26628-22-8 | 6.1 |
| Sodium Cyanide | P106 | 143-33-9 | 6.1 |
| Strychnine & Salts | P108 | 57-24-9 | 6.1 |
| Tetraethyldithiopryophosphate | P109 | 3689-24-5 | 6.1 |
| Tetraethyl Lead (Liquid) | P110 | 78-00-2 | 6.1 |
| Tetraethyl Pryophosphate (Liquid & Solid) | P111 | 107-49-3 | 6.1 |
| Thallic Oxide (Haz. Substance) | P113 | 1314-32-5 | 9 |
| Thallium (1) Selenide (Thallium Compounds) | P114 | 12039-62-0 | 6.1 |
| Thallium (1) Sulfate (Thallium Compounds) | P115 | 7446-18-6 | 6.1 |
| Thiosemicarbazide (Haz. Substance) | P116 | 79-19-6 | 9 |
| Perchloromethylmercaptan | P118 | 594-42-3 | 6.1 |
| Ammonium Vanadate (Ammonium Metavanadate) | P119 | 7803-55-6 | 6.1 |
| Vanadium Pentoxide (Nonfused Form) | P120 | 1314-62-1 | 6.1 |
| Zinc Cyanide | P121 | 557-21-1 | 6.1 |
| Zinc Phosphide | P122 | 1314-84-7 | 4.3, 6.1 |
| Toxaphene (Haz. Substance) | P123 | 8001-35-2 | 9 |
| Carbofuran | P127 | 1563-66-2 | 6.1 |
| Mexacarbate | P128 | 315-18-4 | 6.1 |
| Tirpate | P185 | 26419-73-8 | 6.1 |
| Physostigmine Salicylate | P188 | 57-64-7 | 6.1 |
| Carbosulfan | P189 | 55285-14-8 | 9 |
| Metolcarb | P190 | 1129-41-5 | 6.1 |
| Dimetilan | P191 | 644-64-4 | 6.1 |
| Isolan | P192 | 119-38-0 | 6.1 |
| Oxamyl | P194 | 23135-22-0 | 6.1 |
| Manganese Dimethyldithiocarbamate | P196 | 15339-36-3 | 6.1 |
| Formparanate | P197 | 17702-57-7 | 6.1 |
| Formetanate Hydrochloride | P198 | 23422-53-9 | 6.1 |
| Methiocarb | P199 | 2032-65-7 | 6.1 |
| Promecarb | P201 | 2631-37-0 | 6.1 |
| m-Cumenyl Methylcarbamate | P202 | 64-00-6 | 6.1 |
| Aldicarb Sulfone | P203 | 1646-88-4 | 6.1 |
| Physostigmine | P204 | 57-47-6 | 6.1 |
| Ziram | P205 | 137-30-4 | 6.1 |
| Acetaldehyde (I) | U001 | 75-07-0 | 3 |
| Acetone (I) | U002 | 67-64-1 | 3 |
| Acetonitrile (I, T) (Methyl Cyanide) | U003 | 75-05-8 | 3 |
| Acetophenone (Haz. Substance) | U004 | 98-86-2 | 9 |
| 2-Acetylaminofluorene (Haz. Substance) | U005 | 53-96-3 | 9 |
| Acetyl Chloride | U006 | 75-36-5 | 3, 8 |
| Acrylamide | U007 | 79-06-1 | 6.1 |
| Acrylic Acid | U008 | 79-10-7 | 8 |
| Acrylonitrile | U009 | 107-13-1 | 3 |
| Mitomycin C (Haz. Substance) | U010 | 50-07-7 | 9 |
| Amitrole (Haz. Substance) | U011 | 61-82-5 | 9 |
| Aniline (I, T) | U012 | 62-53-3 | 6.1 |
| Auramine (Haz. Substance) | U014 | 492-80-8 | 9 |
| Azaserine (Haz. Substance) | U015 | 115-02-6 | 9 |
| Benz(c)acridine (Haz. Substance) | U016 | 225-51-4 | 9 |
| Benzal Chloride (Haz. Substance) | U017 | 98-87-3 | 9 |
| Benz(a)athracene (Haz. Substance) | U018 | 56-55-3 | 9 |
| Benzene | U019 | 71-43-2 | 3 |
| Benzenesulfonyl Chloride | U020 | 98-09-9 | 8 |
| Benzidine | U021 | 62-53-3 | 6.1 |
| Benzo(a)pyrene (Haz. Substance) | U022 | 50-32-8 | 9 |
| Benzotrichloride | U023 | 98-07-7 | 8 |
| Dichloromethyoxy Ethane (Haz. Substance) | U024 | 111-91-1 | 9 |
| Dichloroethyl Ether (Haz. Substance) | U025 | 111-44-4 | 9 |
| Chlornaphazine (Haz. Substance) | U026 | 494-03-1 | 9 |
| Dichloroisopropyl Ether | U027 | 108-60-1 | 6.1 |
| Diethylhexyl Phthalate (Haz. Substance) | U028 | 117-81-7 | 9 |
| Methyl Bromide | U029 | 74-83-9 | 2.3 |
| 4-Bromophenyl Phenyl Ether (Haz. Substance) | U030 | 101-55-3 | 9 |
| n-Butyl Alcohol (I) (Butanols) | U031 | 71-36-3 | 3 |
| Calcium Chromate (Haz. Substance) | U032 | 13765-19-0 | 9 |
| Chloral (anhydrous) | U034 | 75-87-6 | 6.1 |
| Chlorambucil (Haz. Substance) | U035 | 305-03-3 | 9 |
| Chlordane, Alpha & Gamma Isomers (Haz. Substance) | U036 | 57-74-9 | 9 |
| Chlorobenzene | U037 | 108-90-7 | 3 |
| Chlorobenzilate (Haz. Substance) | U038 | 510-15-6 | 9 |
| p-Chloro-m-cresol | U039 | 59-50-7 | 6.1 |
| Epichlorohydrin | U041 | 106-89-8 | 6.1 |
| 2-Chloroethyl Vinyl Ether (Haz. Substance) | U042 | 110-75-8 | 9 |
| Vinyl Chloride | U043 | 75-01-4 | 2.1 |
| Chloroform | U044 | 67-66-3 | 6.1 |
| Methyl Chloride (I, T) | U045 | 74-87-3 | 2.1 |
| Chloromethyl Methyl Ether | U046 | 107-30-2 | 3 |
| beta-Chloronaphthalene (Haz. Substance) | U047 | 91-58-7 | 9 |
| o-Chlorophenol | U048 | 95-57-8 | 6.1 |
| 4-Chloro-o-toluidine, Hydrochloride | U049 | 3165-93-3 | 6.1 |
| Chrysene (Haz. Substance) | U050 | 218-01-9 | 9 |
| Creosote (Haz. Substance) | U051 | 8001-58-9 | 9 |
| Cresol | U052 | 1319-77-3 | 6.1 |
| Crotonaldehyde (Stabilized) | U053 | 4170-30-3 | 3 |
| Cumene (I) (Haz. Substance) | U055 | 98-82-8 | 9 |
| Cyclohexane | U056 | 110-82-7 | 3 |
| Cyclohexanone (I) | U057 | 108-94-1 | 3 |
| Cyclophosphamide (Haz. Substance) | U058 | 50-18-0 | 9 |
| Daunomycin (Haz. Substance) | U059 | 20830-81-3 | 9 |
| DDD (Haz. Substance) | U060 | 72-54-8 | 9 |
| DDT (Haz. Substance) | U061 | 50-29-3 | 9 |
| Diallate (Haz. Substance) | U062 | 2303-16-4 | 9 |
| Diben(a, h)anthracene (Haz. Substance) | U063 | 53-70-3 | 9 |
| Dibenzo(a, i)pyrene (Haz. Substance) | U064 | 189-55-9 | 9 |
| 1,2-Dibromomo-3-chloropropane | U066 | 96-12-8 | 6.1 |
| Ethane, 1,2-dibromo- (Ethylene Dibromide) | U067 | 106-93-4 | 6.1 |
| Methylene Bromide (Dibromomethane) | U068 | 74-95-3 | 6.1 |
| Dibutyl Phthalate (Haz. Substance) | U069 | 84-74-2 | 9 |
| o-Dichlorobenzene | U070 | 95-50-1 | 6.1 |
| m-Dichlorobenzene (Haz. Substance) | U071 | 541-73-1 | 9 |
| p-Dichlorobenzene | U072 | 106-46-7 | 6.1 |
| 3,3-Dichlorobenzidine (Haz. Substance) | U073 | 91-94-1 | 9 |
| 1,4-Dichloro-2-butene (I,T) (Haz. Substance) | U074 | 764-41-0 | 9 |
| Ethane, 1,1-Dichloro- (1,1-Dichloroethane) | U076 | 75-34-3 | 3 |
| Ethane, 1,2-Dichloro- (Ethylene Dichloride) | U077 | 107-06-2 | 3 |
| 1,1-Dichloroethylene (Haz. Substance) | U078 | 75-35-4 | 9 |
| 1,2-Dichloroethylene (Haz. Substance) | U079 | 156-60-5 | 9 |
| Methylene Chloride (Dichloromethane) | U080 | 75-090-2 | 6.1 |
| 2,4-dichlorophenol (Haz. Substance) | U081 | 120-83-2 | 9 |
| 2,6-Dichlorophenol (Haz. Substance) | U082 | 87-65-0 | 9 |
| Propylene Dichloride | U083 | 78-87-5 | 3 |
| 1,3-Dichloropropene (Dichloropropene) | U084 | 542-75-6 | 3 |
| 1,2:3,4-Diepoxybutane (Haz. Substance) | U085 | 1464-53-5 | 9 |
| N,N’-Diethyhydrazine (Haz. Substance) | U086 | 1615-80-1 | 9 |
| O,O-Diethyl S-methyl Dithiophosphate (Haz. Subs.) | U087 | 3288-58-2 | 9 |
| Diethyl Phthalate (Haz. Substance) | U088 | 84-66-2 | 9 |
| Diethystilbesterol (Haz. Substance) | U089 | 56-53-1 | 9 |
| Dihydrosafrole (Haz. Substance) | U090 | 94-58-6 | 9 |
| 3,3’-Dimethoxybenzidine (Haz. Substance) | U091 | 119-90-4 | 9 |
| Dimethylamine (I) (Anhydrous, Solution) | U092 | 124-40-3 | 2.1, 3 |
| p-Dimethylaminoazobenzene (Haz. Substance) | U093 | 60-11-7 | 9 |
| 7,12-Dimethylbenz(a)anthracene (Haz. Substance) | U094 | 57-97-6 | 9 |
| 3,3’-Dimethylbenzidine (Haz. Substance) | U095 | 119-93-7 | 9 |
| Dimethylcarbamoyl Chloride | U097 | 79-44-7 | 8 |
| 1,1-Dimethylhydrazine (Symmetrical, Unsymm.) | U098 | 57-14-7 | 3, 6.1 |
| 1,2-Dimethylhydrazine (Symmetrical, Unsymm.) | U099 | 540-73-8 | 3, 6.1 |
| 2,4-Dimethylphenol (Haz. Substance) | U101 | 105-67-9 | 9 |
| Dimethyl Phthalate (Haz. Substance) | U102 | 131-11-3 | 9 |
| Dimethyl Sulfate | U103 | 77-78-1 | 6.1 |
| 2,4-Dinitrotoluene | U105 | 121-14-2 | 6.1 |
| 2,6-Dinitrotoluene | U106 | 606-20-2 | 6.1 |
| Di-n-Octyl Phthalate (Haz. Substance) | U107 | 117-84-0 | 9 |
| 1,4-Dioxane | U108 | 123-91-1 | 3 |
| 1,2-Diphenylhydrazine (Haz. Substance) | U109 | 122-66-7 | 9 |
| Dipropylamine | U110 | 142-84-7 | 3 |
| Di-n-propylnitrosoamine (Haz. Substance) | U111 | 621-64-7 | 9 |
| Ethyl Acetate (I) | U112 | 141-78-6 | 3 |
| Ethyl Acrylate (I) | U113 | 140-88-5 | 3 |
| Ethylene Bisdithiocarbamic Acid, Salts & Esters (Haz. Substance) | U114 | 111-54-6 | 9 |
| Ethylene Oxide (I, T) | U115 | 75-21-8 | 2.3 |
| Ethylenthiourea (Haz. Substance) | U116 | 96-45-7 | 9 |
| Ethyl Ether (I) (Diethyl Ether) | U117 | 60-29-7 | 3 |
| Ethyl Methacrylate | U118 | 97-63-2 | 3 |
| Ethyl Methanesulfonate (Haz. Substance) | U119 | 62-50-0 | 9 |
| Fluoranthene (Haz. Substance) | U120 | 206-44-0 | 9 |
| Trichloromonofluoromethane (Haz. Substance) | U121 | 75-69-4 | 9 |
| Formaldehyde (Solutions-Flammable, Non-Flammable) | U122 | 50-0-0 | 3, 9 |
| Formic Acid (C, T) | U123 | 64-18-6 | 8 |
| Furan (I) | U124 | 110-00-9 | 3 |
| Furfural (I) | U125 | 98-01-1 | 3 |
| Glycidylaldehyde | U126 | 765-34-4 | 3 |
| Hexachlorobenzene | U127 | 118-74-1 | 6.1 |
| Hexachlorobutadiene | U128 | 87-68-3 | 6.1 |
| Lindane (Haz. Substance) | U129 | 58-89-9 | 9 |
| Hexachlorocyclopentadiene | U130 | 77-47-4 | 6.1 |
| Hexachloroethane (Haz. Substance) | U131 | 67-72-1 | 9 |
| Hexachlorophene | U132 | 710-30-4 | 6.1 |
| Hydrazine (R, T) | U133 | 302-01-2 | 3, 6.1, 8 |
| Hydrofluoric Acid (C, T) | U134 | 7664-39-3 | 8 |
| Hydrogen Sulfide | U135 | 7783-06-4 | 2.3, 2.1 |
| Cacodylic Acid | U136 | 75-60-5 | 6.1 |
| Ideno[1,2,3-cd]pyrene (Haz. Substance) | U137 | 193-39-9 | 9 |
| Methyl Iodide | U138 | 74-88-4 | 6.1 |
| Isobutyl Alcohol (I, T,) (Isobutanol) | U140 | 78-83-1 | 3 |
| Isosafrole (Haz. Substance) | U141 | 120-58-1 | 9 |
| Kepone (Haz. Substance) | U142 | 143-50-0 | 9 |
| Lasiocarpine (Haz. Substance) | U143 | 303-34-4 | 9 |
| Lead Acetate | U144 | 301-04-2 | 6.1 |
| Lead Phosphate (Haz. Substance) | U145 | 7446-27-7 | 9 |
| Lead Subacetate (Haz. Substance) | U146 | 1335-32-6 | 9 |
| Maleic Anhydride | U147 | 108-31-6 | 8 |
| Maleic Hydrazide (Haz. Substance) | U148 | 123-33-1 | 9 |
| Malononitrile | U149 | 109-77-3 | 6.1 |
| Melphalan (Haz. Substance) | U150 | 148-82-3 | 9 |
| Mercury | U151 | 7439-97-6 | 8 |
| Methacrylonitrile | U152 | 126-98-7 | 3 |
| Methanethiol | U153 | 74-93-1 | 2.3, 2.1 |
| Methanol (I) | U154 | 67-56-1 | 3 |
| Methapyrilene (Haz. Substance) | U155 | 91-80-5 | 9 |
| Methyl Chlorocarbonate (Methyl Chloroformate) | U156 | 79-22-1 | 6.1 |
| 3-Methylcholanthrene (Haz. Substance) | U157 | 56-49-5 | 9 |
| 4,4’-Methylenebis(2-Chloraniline) (Haz. Substance) | U158 | 101-14-4 | 9 |
| Methyl Ethyl Ketone (I, T) (Ethyl Methyl Ketone) | U159 | 78-93-3 | 3 |
| Methyl Ethyl Ketone Peroxide (R, T) | U160 | 1338-23-4 | 5.2 |
| Methyl Isobutyl Ketone | U161 | 108-10-1 | 3 |
| Methyl Methacrylate (I, T) (Monomer) | U162 | 80-62-6 | 3 |
| N-Methyl-N’-Nitro-N-Nitrosognanidine | U163 | 10-25-7 | 4.1 |
| Methylthiouracil (Haz. Substance) | U164 | 56-04-2 | 9 |
| Naphthalene (Crude or Refined) | U165 | 91-20-3 | 4.1 |
| 1,4-Naphthalenedione (Haz. Substance) | U166 | 130-15-4 | 9 |
| alpha-Naphthylamine | U167 | 134-32-7 | 6.1 |
| beta-Naphthylamine | U168 | 91-59-8 | 6.1 |
| Nitrobenzene (I, T) | U169 | 98-95-3 | 6.1 |
| p-Nitrophenol | U170 | 100-02-7 | 6.1 |
| Nitropropane (I, T) | U171 | 79-46-9 | 3 |
| N-Nitrosodi-n-butylamine (Haz. Substance) | U172 | 924-16-3 | 9 |
| N-Nitrosodiethanolamine (Haz. Substance) | U173 | 1116-54-7 | 9 |
| N-Nitrododiethylamine (Haz. Substance) | U174 | 55-18-5 | 9 |
| N-Nitroso-N-ethylurea (Haz. Substance) | U176 | 759-73-9 | 9 |
| N-Nitroso-N-Methylurea (Haz. Substance) | U177 | 684-93-5 | 9 |
| N-Nitroso-N-Methylurethane (Haz. Substance) | U178 | 615-53-2 | 9 |
| N-Nitrosopiperidine (Haz. Substance) | U179 | 100-75-4 | 9 |
| N-Nitrasopyrrolidine (Haz. Substance) | U180 | 930-55-2 | 9 |
| 5-Nitro-o-toluidine (mono) | U181 | 99-55-8 | 6.1 |
| Paraldehyde | U182 | 123-63-7 | 3 |
| Pentachlorobenzene (Haz. Substance) | U183 | 608-93-5 | 9 |
| Pentachloroethane | U184 | 76-01-7 | 6.1 |
| Pentachloronitrobenzene (Haz. Substance) | U185 | 82-68-8 | 9 |
| 1,3-Pentadiene (I) (Haz. Substance) | U186 | 504-60-9 | 9 |
| Phenacetin (Haz. Substance) | U187 | 62-44-2 | 9 |
| Phenol (molten, solid, solutions) | U188 | 108-95-2 | 6.1 |
| Phosphorus Sulfide | U189 | 1314-80-3 | 4.3, 4.1 |
| Phthalic Anhydride | U190 | 85-44-9 | 8 |
| 2-Picoline | U191 | 109-06-8 | 3 |
| Pronamide (Haz. Substance) | U192 | 23950-58-5 | 9 |
| 1,3-Propane Sultone (Haz. Substance) | U193 | 1120-71-4 | 9 |
| n-Propylamine (I, T) | U194 | 107-10-8 | 3 |
| Pyridine | U196 | 110-86-1 | 3 |
| p-Benzoquinone | U197 | 106-51-4 | 6.1 |
| Reserpine (Haz. Substance) | U200 | 50-55-5 | 9 |
| Resorcinol | U201 | 108-46-3 | 6.1 |
| Saccharin, & Salts (Haz. Substance) | U202 | 81-07-2 | 9 |
| Safrole (Haz. Substance) | U203 | 94-59-7 | 9 |
| Selenium Dioxide (Selenium Oxide) | U204 | 7446-08-4 | 6.1 |
| Selenium Sulfide | U205 | 7488-56-4 | 6.1 |
| Streptozotocin (Haz. Substance) | U206 | 18883-66-4 | 9 |
| 1,2,4,5-Tetrachlorobenzene (Haz. Substance) | U207 | 95-94-3 | 9 |
| 1,1,1,2-Tetrachloroethane (Haz. Substance) | U208 | 630-20-6 | 9 |
| 1,1,2,2-Tetrachloroehtane (Haz. Substance) | U209 | 79-34-5 | 9 |
| Tetrachloroethylene | U210 | 127-18-4 | 6.1 |
| Carbon Tetrachloride | U211 | 56-23-5 | 6.1 |
| Tetrahydrofuran (I) | U213 | 109-99-9 | 3 |
| Thallium (I) Acetate (Thallium Compound) | U214 | 563-68-8 | 6.1 |
| Thallium (I) Carbonate (Thallium Compound) | U215 | 6533-73-9 | 6.1 |
| Thallium (I) Chloride (Thallium Compound) | U216 | 7791-12-0 | 6.1 |
| Thallium (I) Nitrate (Thallium Compound)) | U217 | 10102-45-1 | 6.1, 5.1 |
| Thioacetamide (Haz. Substance) | U218 | 62-55-5 | 9 |
| Thiourea (Haz. Substance) | U219 | 62-56-6 | 9 |
| Toluene | U220 | 108-88-3 | 3 |
| Toluenediamine (Haz. Substance) | U221 | 25376-45-8 | 9 |
| o-Toluidine Hydrochloride (Haz. Substance) | U222 | 636-21-5 | 9 |
| Toluene Diisocyanate | U223 | 26471-62-5 | 6.1 |
| Bromoform | U225 | 75-25-2 | 6.1 |
| Methyl Chloroform (1,1,1-Trichloroethane) | U226 | 71-55-6 | 6.1 |
| 1,1,2-Trichloroethane (Haz. Substance) | U227 | 79-00-5 | 9 |
| Trichloroethylene | U228 | 79-01-6 | 6.1 |
| Tris(2,3-dibromopropyl)phosphate (Haz. Substance) | U235 | 126-72-7 | 9 |
| Trypan Blue (Haz. Substance) | U236 | 72-57-1 | 9 |
| Uracil Mustard (Haz. Substance) | U237 | 66-75-1 | 9 |
| Ethyl Carbamate (Urethane) (Haz. Substance) | U238 | 51-79-6 | 9 |
| Xylene (I) | U239 | 1330-20-7 | 3 |
| 2,4-D Salts & Esters (Haz. Substance) | U240 | 94-75-7 | 9 |
| 1-Propene 1,1,2,3,3,3-hexachloro (Haz. Substance) | U243 | 1888-71-7 | 9 |
| Thiram (Haz. Substance) | U244 | 137-26-8 | 9 |
| Cyanogen Bromide | U246 | 506-68-3 | 6.1 |
| Methoxychlor (Haz. Substance) | U247 | 72-43-5 | 9 |
| Warfarin & Salts (<0.3%) (Haz. Substance) | U248 | 81-81-2 | 9 |
| Zinc Phosphide | U249 | 1314-84-7 | 4.3, 6.1 |
| Benoyml | U271 | 17804-35-2 | 9 |
| Sulfallate | U277 | 95-06-7 | 9 |
| Bendiocarb | U278 | 22781-23-3 | 6.1 |
| Carbaryl | U279 | 63-25-2 | 9 |
| Barban | U280 | 101-27-9 | 9 |
| o-Toluidine | U328 | 95-53-0 | 6.1 |
| p-Toluidine | U353 | 106-49-0 | 6.1 |
| Ethylene Glycol Monoethyl Ether | U359 | 110-80-5 | 3 |
| Bendiocarb Phenol | U364 | 22961-82-6 | 6.1 |
| Molinate | U365 | 2212-67-1 | 9 |
| Dazomet | U366 | 533-74-4 | 9 |
| Carbofuran Phenol | U367 | 1563-38-8 | 6.1 |
| Carbendazin | U372 | 10605-21-7 | 9 |
| Propham | U373 | 122-42-9 | 9 |
| 3-Iodo-2-propynyl n-butylcarbamate | U375 | 55406-53-6 | 9 |
| Selenium, Tetrakis (Dimethyldithiocarbamate) | U376 | 144-34-3 | 6.1 |
| Potassium n-Methyldithiocarbamate | U377 | 137-41-7 | 9 |
| Potassium n-Hydroxymethyl-n-methyldithiocarbamate | U378 | 51026-28-9 | 9 |
| Sodium Dibutyldithiocarbamate | U379 | 136-30-1 | 9 |
| Sodium Diethyldithiocarbamate | U381 | 148-18-5 | 9 |
| Sodium Dimethyldithiocarbamate | U382 | 128-04-1 | 9 |
| Potassium Dimethyldithiocarbamate | U383 | 128-03-0 | 9 |
| Metam-sodium | U384 | 137-42-8 | 8 |
| Vernolate | U385 | 1929-77-7 | 9 |
| Cycloate | U386 | 1134-23-2 | 9 |
| Prosulfocarb | U387 | 52888-80-9 | 9 |
| Triallate | U389 | 2303-17-5 | 9 |
| EPTC | U390 | 759-94-4 | 9 |
| Pebulate | U391 | 1114-71-2 | 9 |
| Butylate | U392 | 2008-41-5 | 9 |
| Copper Dimethyldithiocarbamate | U393 | 137-29-1 | 6.1 |
| A2213 | U394 | 30558-43-1 | 9 |
| Diethylene Glycol, Dicarbamate | U395 | 5952-26-1 | 6.1 |
| Ferbam | U396 | 14484-64-1 | 9 |
| Bis(pentamethylene) Thiruam Tetrasulfide | U400 | 120-54-7 | 9 |
| Tetramethylthiuram Monosulfide | U401 | 97-74-5 | 9 |
| Tetrabutylthiuram Disulfide | U402 | 1634-02-2 | 9 |
| Disulfiram | U403 | 97-77-8 | 9 |
| Triethylamine | U404 | 121-44-8 | 3 |
| Ethyl Ziram | U407 | 14324-55-1 | 9 |
| Thiophanate-Methyl | U409 | 23564-05-8 | 9 |
| Thiodicarb | U410 | 59669-26-0 | 9 |
| Propoxur | U411 | 114-26-1 | 6.1 |

N/A: Not Applicable, None Found

Table II.A.4.b.-4

Emergency Equipment Cabinet

2	Empty 55-gallon, 17-H, lined drums

2	Salvage drums (lined or poly)

4	8-inch diameter, 10-foot long sorbent booms

2	Spark-resistant safety shovels

2	Crowbars (nonsparking)

2	18-inch pipe wrenches (nonsparking)

2	Drum plug wrenches (nonsparking)

4	Explosion-proof flashlights

1	Megaphone

2	Nylon ropes (each 50 feet long, ½ inch thick)

1	Oxygen kit

Personnel Safety Equipment Cabinet

5	Safety glasses

10	Safety goggles

5	Face shield/hard hat combination

2	Emergency eye/face/body wash

20	Tyveks total body coverage

4	Duct tape rolls

10	Rubber boots

10	Rubber gloves

5	Corrosive-resistant aprons

2	Corrosive-resistant suits

5	Leather gloves

10	Half-mask respirators

5	Full-face respirators

1	Box of respirator cartridges (OV and AG)