EXCEL

ENGINEERING CONSULTANTS, INC.

Environmental & Civil Engineers

Hazardous

Waste Transfer Facility

Closure Plan

Prepared For:

Environmental Enterprises of Florida, Inc.

314 B Landstreet Road

Orlando, Florida 32824

AUGUST 1995

150 Oxford Road, Suite 120 ' Fern Park, Florida 32730

OFFICE (407) 260-2292 ' FAX (407) 260-1193

HAZARDOUS

WASTE TRANSFER FACILITY

CLOSURE PLAN

Table of Contents

I.         Introduction

II.        Project Description

III.       Operations

IV.       Closure Performance Standard

V.

Closure Plan

· Expected Year of Closure

· Estimate of Maximum Inventory

· Removal of Inventory

. Decontamination of the Facility

. Closure Schedule

· Amendment of the Closure Plan

. Changes in Operating Plans of Facility Design Affect of the Closure Plan

. Notifies of partial or Final Closure

· Closure Cost Estimate

\/I.	Site Plan

I. 	INTRODUCTION

The Closure Plan addresses operations that will be conducted to ensure that all wastes will be properly disposed of, and that all traces of contamination will be removed from the units where hazardous wastes were handled when the facility ceases its operation for an indefinite time and wishes not to be regulated under the Resource Conservation and Recovery Act (RCRA). Submittal of a Closure Plan in accordance with the provisions in 40 CFR Part 265.111, 265. 112(c), 265.114 and 265.115 is mandated in the Florida Department of Environmental Protection (FDEP) 62-730.

II.	PROJECT DESCRIPTION

--.--

Environmental Enterprises of Florida, Inc. (EEFI) is a hazardous waste transfer facility located at 314 B West Landstreet, Orlando, Florida 32824 in Section 2, Township 24 south, Range 29 east, Orange County. The project is located approximately 7,900 feet east of the intersection of US 441 and West Landstreet Road. The project is a permitted hazardous waste transfer facility in accordance with 62-730, FA C. The facility's EPA ID Number is FLR000006353. The facility site is approximately 600 feet by 150 feet with an approximate area of 90,000 square feet (2 acres). The site has one operations building, one temporary storage area for metal roll-off containers, one temporary storage area for tractor trailers, and parking area for the empty trailers and trucks. The temporary storage area is diked in order to contain any discharges (see attached plan).

The site’s soils are classified by the United States Geological Survey to be predominantly Smyrna Fine Sands with inclusions of Bassinger sands and Pomello sands. Smyrna Fine Sands have a depth to the water table of approximately one to two feet. These soils are typically silty poorly drained soils.

III.	OPERATIONS

The facility is a permitted hazardous waste transporter with an approved Contingency and Emergency Plan. The transporter collects hazardous and non-hazardous waste from various generators. The wastes are stored in sealed 55 gallon drums or sealed roll-off bins which the transporter picks up at the generators site. Trucks and trailers are loaded with the wastes and the wastes are hauled to various permitted TSD facilities for final disposal. Wastes are temporarily stored on site for periods exceeding 24 hours but less than 10 days. The waste is never off-loaded at this site. Therefore there is never any contact between the drums and the site. The drums remain in the trailers until the trailer leaves the site. Furthermore, the drums are never opened on-site.

The trailers which have drums or roll off bins with hazardous waste materials will be parked in the areas designated on the site plan. These areas are paved with 6 inch

EEFI/Closure Plan August 8, 1995

Page 2

thick concrete and bermed with a continuous asphalt berm. Any leaks that may occur will be contained within these designated areas. Any discharges will be remediated in accordance with EEFl's Emergency Plan on file with the FDEP. No trailers with

hazardous waste drums or roll off bins will be stored outside the designated impervious and contained areas. The shell staging areas shown on the attached site plan are for storage of empty tractor trailers and for maneuvering the tractor trailers.

Clean drums are stored inside the miscellaneous storage area. These drums are delivered to the generators' location for use by the generator. None of the filled drums are off-loaded at this site. The drums remain in the trailers until final off-site disposal. There is no cleaning of drums, equipment or trailers at the facility. Any leaks or discharges are covered under the approved Emergency And Contingency Plan and the transporter will follow the approved plans in the event than a leak or discharge occurs.

IV.	CLOSURE PERFORMANCE STANDARD

Upon final closure of the facility, Environmental Enterprises of Florida, Inc. plans to remove all the waste in storage at that time, conduct a facility inspection to determine if there are any areas which require cleanup and clean any areas that may show signs of contamination. Since the facility does not off load any drums 'from the trailers there is no drum storage area. Additionally there is no cleaning of drums, trailers or equipment

at the facility. Therefore there are no specific areas to decontaminate.

V.	CLOSURE PLAN

Expected Year Of Closure

This facility is expected to operate for twenty five years from the start of the operation. Partial closure will not occur because the facility is too small for part of it to be isolated and still allow for the parking of the trailers.

Estimate Of Maximum Inventory

The maximum amount of hazardous waste to be stored at this facility over the facility's 25 year life is expected to be approximately 4, 787,500 gallons of liquid waste stored in 55 gallon drums and 36,250 cubic yards of solid waste stored in roll-off bins and 1 yard. bags.

Removal of Inventory

Inventory of the waste remains in the trailers until its final off-site disposal. The trailers along with the containerized hazardous waste inside the trailers will be moved to another permitted location or taken to its final destination at the time of closure. It appears most likely that the hazardous waste will be transported to the Perma Fix Environmental facility FLD980711071 located in Gainesville, Florida. However, it may

EEFI/Closure Plan August 8, 1995

Page 3

also be transferred to other permitted TSD facilities which EEFI Utilizes. This will be determined at time of closure.

Decontamination Of The Facility

Since there is no off loading of drums at the facility there will not be any specific areas to decontaminate at closure. Leaks and discharges that occur during the operation of the facility are covered under the approved Contingency and Emergency Plan. A site

inspection will be performed to determine if there are areas  which require cleaning. This will be accomplished in a manner approved by the FDEP. Any areas that have hazardous waste spills will be handled in accordance with the facility's Emergency Plan on file at the FDEP.

Any contaminated soils will be excavated and stored in drums for off-site disposal at a permitted hazardous waste disposal facility.

Closure Schedule

Closure of the facility will be completed within a 30 day period in accordance with the following schedule:

Inventory Removal	5 days

Inspection Of Facility	5 days

Cleanup	5 days

Certification Of Closure	5 days

Amendment Of The Closure Plan

The facility will submit a written notification to the regulating agency whenever changes are needed or occur at the facility that affect the closure plan. The notification will contain an amendment to the closure plan reflecting modifications needed because of changes at the facility. The written notification will be submitted whenever of the following occurs:

Changes in operating plans or facility design affect the closure plan.

1.		There is a change in the expected year of closure.

2.		Partial or final closure activities are conducted and unexpected events require

a modification of the approved closure plans.

3.	The facility will submit the written notification for approval at least 60 days prior to the proposed changes, or no later than 60 days after an unexpected event has occurred that forces changes at the facility, which affect the closure plan.

EEFI/Closure Plan August 8, 1995

Page 4

Notification of Final Closure

The facility will notify the regulating agency in writing at least 45 days prior to the date on which it expects to begin partial or final closure at the facility.

Closure Cost Estimate

-Inventory Removal:

500.00

-Inspection of Facility

300.00

-Cleanup (contingency)

1,000.00

-Certification of Closure

500.00

Subtotal:

2,300.00

-Administrative Costs

500.00

Total:

2,800.00