SLUDGE DRYER CLOSURE REPORT

USED OIL PROCESSING FACILITY PERMIT

72815-HO-007

FOR

INDUSTRIAL WATER SERVICES, INC.

JACKSONVILLE, FLORIDA

Submitted by:

SHAUNTE STALLWORTH, COMPLIANCE MANAGER

INDUSTRIAL WATER SERVICES, INC.

Jacksonville, Florida

November 28, 2007

Sludge Dryer Closure Report

Used Oil Processing Facility Permit # 72815-HO-007

Industrial Water Services, Inc.

Jacksonville, Florida

Closure of Tank 48, Sludge Dryer

Background

Industrial Water Services, Inc. (IWS) owns and operates an industrial used oil/wastewater

pretreatment facility in Jacksonville, Florida.   The IWS facility is permitted by the Department of Environmental Protection to operate as a used oil processor through the Used Oil Processing Facility Permit No. 72815-HO-007.  The closing of tank 48 in this permit is defined by 40 CFR 279.54(h) and 62-710.800(9), F.A.C.

IWS, Inc. submitted an initial written request to Mr. Bheem Kothur of FDEP, Division of Waste Management to close tank 48 in Attachment A of the Used Oil Processing Facility Permit on September 14, 2007.  Upon approval, the completion date of the closing of tank 48 was agreed to be October 30, 2007.   On October 12, 2007, IWS, Inc. had to request an extension on the approved closure schedule to properly dispose of entrapped oil discovered in various parts of the dryer.  Mr. Kothur approved the new completion date of the closing of the dryer to be November 30, 2007.

Analytical Review

Industrial Water Services, Inc submitted composite rinseate samples to Summit Environmental Technologies, Inc. after each piece of equipment was tripled rinsed required in Part V:  Closure Requirements of the Used Oil Processing Facility Permit.  In reviewing the report, the data showed that there were no hazardous constituents present and IWS deemed the material to be non-hazardous waste.  There were presence of Barium at a level of 0.046 ppm, however it posed no threat to be potentially classified as D005 per 40 CFR 261.24 (b).  Since we are an appropriately permitted non-hazardous waste water pretreatment facility, it was cost effective for us to process our own non-hazardous waste water from the closure of the unit.

Disposal of Metallic Contents of Dryer

IWS, Inc. is submitting copies of weight tickets of the scrap metal from the Sludge Dryer unit to meet the requirement of Part V- Closure Requirement for recordkeeping.  The Sludge Dryer Unit metal was intentionally sold to a scrap dealer, Berman Brothers, Inc., to keep the material from being used for application, such as drinking water tanks.  Table 1 below illustrates the characteristics of the metal sold or disposed of, and provide an inventory of certain equipments/parts that was retained for future application in the plant.

Table 1:	Disposal Table for the Dryer Closure

| Item Description | Net Weight (lbs) | Quantity | Retained or Disposed/Sold | Disposal Date |
| --- | --- | --- | --- | --- |
| Red Brass | 240 | ----------------- | Disposed/sold | 11/14/07 |
| Steel | 8520 | ------------------ | Disposed/sold | 11/14/07 |
| Steel | 6960 | ------------------ | Disposed/sold | 11/14/07 |
| Steel | 5960 | ----------------- | Disposed/sold | 11/14/07 |
| Steel | 10780 | ----------------- | Disposed/sold | 11/15/07 |
| Steel | 3420 | ----------------- | Disposed/sold | 11/16/07 |
| Electric motor | -------------- | 2 | Retained | 11/14/07 |
| Control switch | -------------- | 2 | Retained | 11/14/07 |
| 8-in. diameter schedule 20 pipe (stack) | ---------------- | 1 | Retained | 11/14/07 |

Industrial Water Services, Inc has completely removed the dryer and its ancillary equipment.  All parts that were not retained for future use in the facility were sold to Berman Brothers, Inc. for scrap.  Throughout the process of dismantling the unit, photographs were taken to document the process of the closure procedures.  The Used Oil Processing Facility Permit has been modified to reflect the closure of the dryer stated in this report.  Analytical reports and weight tickets have been provided to reflect that IWS, inc. has met all the requirements stated in Part V- Closure Requirement listed in the Used Oil Processing Facility Permit No. 72815-HO-007.