Revision 0 – 06/30/10

SAFETY-KLEEN SYSTEMS, INC.

BOYNTON BEACH, FL

PREPAREDNESS, PREVENTION, CONTINGENCY PLAN, AND EMERGENCY PROCEDURES FOR DAILY BUSINESS OPERATIONS

Revision 0 – 06/30/10

TABLE OF CONTENTS

EMERGENCY PHONE NUMBERS								iii      5.1	GENERAL INFORMATION								5-1

5.2	INSPECTION PROCEDURES								5-4

5.3	EMERGENCY NOTIFICATION							5-7

5.4	EMERGENCY RESPONSE AGENCIES AND TEAM MEMBERS			5-7

5.5	ACTIONS OF THE EMERGENCY COORDINATOR					5-8

5.6	POTENTIAL SPILL SOURCES							5-12

5.7	DECONTAMINATION								5-17

5.8	EMERGENCY RESPONSE EQUIPMENT AND COMMUNICATION			5-18

5.9	FIRE CONTROL & EXPLOSION PROCEDURES					5-19

5.10	EVACUATION PLAN									5-22

5.11	AVAILABILITY AND REVISION OF THE PREPAREDNESS,

PREVENTION, AND CONTINGENCY PLAN						5-23

5.12	ARRANGEMENTS WITH LOCAL AUTHORITIES					5-24

APPENDICES

Appendix A	Example Letters to Local Authorities

i

Revision 0 – 06/30/10

LIST OF FIGURES

Figure 5.1-1	Facility Layout and Access Control Features

Figure 5.1-2	Truck Traffic Patterns and Loading/Unloading Areas of Hazardous Waste

Figure 5.2-1	Weekly Inspection of Safety and Emergency Equipment, Security Devices and

Miscellaneous Equipment

Figure 5.6-1	Location of Emergency Equipment

Figure 5.6-2	Incident Report Form

Figure 5.6-3	Container Storage Area

Figure 5.6-4	Return/Fill Station

Figure 5.6-5	Tank Storage Area

Figure 5.9-1	Fire Fighting Sprinkler System

LIST OF TABLES

Table 5.1-1	Permitted and Transfer Wastes

Table 5.2-1	Inspection Schedule

Table 5.6-1	Emergency Response Equipment

Table 5.8-1	Description and Uses of Emergency Equipment

ii

Revision 0 – 06/30/10

5.0	PREPAREDNESS, PREVENTIION, CONTIGENCY PLAN, AND EMERGENCY

PROCEDURES FOR DAILY BUSINESS OPERATIONS

5.1	GENERAL INFORMATION

Purpose

The preparedness, prevention, contingency plan, and emergency procedures are designed to

ensure that Safety-Kleen reduces the possibility of emergency situations and, should they occur

responds in a manner to prevent, or minimize hazards to human health or the environment from

fire, explosion, or any unplanned sudden or non-sudden release of hazardous material constituents

to the air, soil, surface water, or ground water at the facility.

The provisions of the plan are to be carried out immediately if there is a fire, explosion, or release

of hazardous materials that could threaten human health or the environment.  All responses must

conform to the procedures contained in this plan.

General Descriptions of Activities

The business activities conducted at the Boynton Beach Branch relate to the leasing and servicing

of Safety-Kleen Parts Cleaning Equipment, including the provisions of a solvent leasing service

for customers.  Clean solvents are distributed from, and used solvents returned to, the Branch,

where separate storage tanks are utilized for the storage of clean and used parts washer solvent.

One 15,000-gallon and one 20,000-gallon are utilized for the storage of clean parts washer

solvent.  One 15,000-gallon tank is utilized for the storage of used parts washer solvent.  One

20,000-gallon tank is utilized for the storage of used oil.  One 5,000-gallon tank and one 8,000-	gallon tank are utilized for the storage of oily water.  Warehouse space is utilized for the storage 	of containers of both clean and used immersion cleaner, parts washer solvent, paint waste, Fluid 	Recovery Services (FRS) wastes, branch generated waste, and dry cleaning wastes.  Overpack 	containers are used for the management of containers whose integrity has been compromised.

5-1

Revision 0 – 06/30/10

Parts washer solvents are transported in covered containers between the Branch and customers.

Upon returning to the Branch, the used parts washer solvent is transferred from the containers

into a wet dumpster (solvent return receptacle) where solids from the solvents are retained.  Used

parts washer solvent from the wet dumpster is pumped into the 15,000-gallon aboveground

storage tank.  Used parts washer solvent is picked up regularly by a bulk tanker truck from a

Safety-Kleen recycle center, which at the same time delivers clean solvent.  The sludge in the

wet dumpster is regularly cleaned out, containerized, and stored as Branch-generated waste in

the container storage area.

Immersion cleaner (IC) remains in a covered container at all times during transportation and

storage.  IC is not transferred to another container while being used by customers, or while in

storage at the branch.

Dry cleaning wastes are picked up at commercial dry cleaning establishments in containers.  Dry

cleaning wastes handled by Safety-Kleen consist of spent filter cartridges, powder residue from

diatomaceous or other powder filter systems, still bottoms, and separator water, all of which fall

into the categories of either perchloroethylene-based waste or naptha-based waste.  The dry

wastes are packaged at customers’ locations.

All antifreeze collected and managed by Safety-Kleen within Florida is recycled.  At the

customer’s location, Safety-Kleen pumps waste ethylene glycol (antifreeze) into a Safety-Kleen

used oil tanker truck.  The waste ethylene glycol is transported from the customer to the branch

for storage until pick up.  The ethylene glycol is then transported to a used antifreeze recycling

facility for reprocessing into a pure product which is then sold on the open market.  This

procedure is in accordance with FDEP’s Florida Fact Sheet on the Best Management Practices

for Managing Used Antifreeze Destined for Recycling, dated February, 2007.

5-2

Revision 0 – 06/30/10

Safety-Kleen also provides a paint waste reclamation service.  Wastes containing various thinners

and paints are collected in containers and are stored in the container storage area.  Paint wastes

are received at the Branch on manifests which are terminated at that point.  These wastes are

then re-manifested and shipped to a reclaimer, and the regenerated solvent may be distributed

to Safety-Kleen customers for use as a product.

FRS wastes are packaged in polyethylene or steel containers which are not opened until they

reach a recycle center.  The FRS wastes are transfer wastes and may be stored onsite for up to

10 days.  The FRS wastes may also undergo branch-to-branch or truck-to-truck transfer.  This

Transfer will occur inside secondary containment.

The waste products exhibit essentially the same biological, physical, and chemical properties as

the fresh product.  Used products are basically fresh products with impurities of dirt and metals.

Material Data Safety Sheets (MSDSs) for each hazardous material are available at the Branch and

on demand by fax through a company-owned MSDS information service.  This service provides

24-hour phone or fax access to an extensive MSDS database.

The Branch is registered in Florida as a transporter and storage facility for mercury-containing

lamps and devices destined for recycling.  This registration includes a commitment to comply

with the requirements of Florida Administrative Code (FAC) 62-737.400.  As a registered storage

facility, the Branch can store up to 2,000 kilograms of lamps/devices for a period of up to 180

days.  Safety-Kleen provides customers with empty four-foot and eight-foot boxes which hold

up to 39 lamps.  Boxes containing lamps are picked up from customers and are handled at the

Branch as non-hazardous transfer wastes.  The boxes are stored at the Branch in a designated area

within the transfer waste storage area.  This storage area is labeled in accordance with

FAC 62-737.400(5)(b), and partially isolated from other transfer wastes to avoid potential for

accidental breakage.  The boxes are periodically shipped to a permitted mercury recovery or

reclamation facility.  Prior to shipment out of the Branch, the boxes are placed on pallets and

shrink-wrapped with plastic.

5-3

Revision 0 – 06/30/10

Figures 5.1-1 and 5.1-2 show the basic site and floor plans and the locations of waste

management facilities and facility storage.  Table 5.1-1 provides a list of permitted and transfer

wastes handled at the facility.

5.2	INSPECTION PROCEDURES

Inspection of Safety Equipment

The purpose of the inspection plan is to establish a procedure and schedule for the systematic

monitoring and inspection of emergency and spill control equipment to ensure proper operation,

and to maintain compliance.  Table 5.2-1 is an Inspection Schedule.

`	The Branch Manager or designee is responsible for carrying out the inspection in accordance with

the following procedure and schedule.

- A weekly inspection of fire extinguishers must be performed to ensure that the tag date has not expired and the units are properly charged and accessible.

- A weekly inspection of eyewash units must be performed to assure accessibility; check for proper operation of this equipment on a weekly basis.  Inventory of the first-aid kit must be checked on a weekly basis.

- A weekly check of the supply of spill control equipment (absorbent material) must be performed.

- A weekly check of the conditions and inventory of other emergency equipment will be made.  This includes gloves, aprons, safety glasses, respirators, and other personal protective equipment.

______________________________________________________________________________

5-4

Revision 0 – 06/30/10

Inspection of Security Equipment

The Branch Manager or designee, using the Weekly Inspection Log ( Figure 5.2-1 or

similar), inspects the security features of the facility weekly (e.g., gates and locks),

looking for any evidence of sticking, corrosion, or unusual activity.  The facility fence

will be checked weekly for deterioration, gaps, and broken wire ties.

Inspection of Waste Management Facilities

The purpose of the inspection plan is to establish a procedure and schedule for the

systematic monitoring and inspection of hazardous waste management and other material

management facilities to ensure proper operation and maintain compliance.  Table 5.2-1

provides an Inspection Schedule.

The Branch Manger or designee is responsible for carrying out the inspections of all

hazardous waste management facilities in accordance with the following procedure and

schedule.

Daily inspections of aboveground storage tanks will include the following:

- Note volume in tank.

- Observe tank exterior for loose anchoring, wet spots, and leaks.

- Check the automatic high level alarm.  In addition, measure the depth of used solvent in the tanks to confirm the proper functioning of the automatic alarm system and to determine unexpected deviations in tank measuring data, or a sudden drop in liquid level, which may indicate leakage.

- Inspect secondary containment walls and piping.

- Inspect transfer pumps for leaking seals and overheated motors.

- Inspect the solvent dispensing hose, fittings, and valve for any leaks, damage, or wear that could cause a leak to develop.

______________________________________________________________________________

5-5

Revision 0 – 06/30/10

- Inspect the valves for evidence of leakage.  Stem leaks from worn glands and warped valve bodies should be repaired.  If the valve cannot be repaired, replace the unit.

Also, the tanks will be visually inspected and tested periodically.  Daily inspection of the

Solvent return receptacle (wet dumpster) will consist of an inspection for leaks and

excess dumpster mud build-up.

Daily inspections of the container storage area include the following:

- Verify that the total volume is within permitted limits.

- Physically examine the condition of containers to verify that leaks have not occurred since the last inspection.

- Verify that all container identification, dates, and hazardous waste labels are attached and current.

- Inspect container placement and stacking such as aisle space, height, and stability of stacks.

- Examine containment areas to detect signs of deterioration and failure of the containment system such as cracks, breakage, settlement, and spillage.

Corrective Action

Any discrepancies or deficiencies found during routine inspections will be recorded in the inspection log and brought to the attention of a supervisor.  At this time, an evaluation of the seriousness of the problem will be noted and a decision made if the situation requires immediate action or the problem can be handled as routine maintenance.  The evaluation of the seriousness of the problem will be recorded in the facility’s inspection log.  If the problem poses a threat to human health or the environment, action will be taken immediately.  The Branch Manager has the overall responsibility for resolving any discrepancies found during the routine inspection.

______________________________________________________________________________

5-6

Revision 0 – 06/30/10

5.3	EMERGENCY NOTIFICATION

Emergency Coordinator

The Branch Manager or designee is the emergency coordinator.  Page iii at the beginning

of Section 5 includes the names, home addresses, and both office, home, and mobile

phone numbers of the primary and secondary coordinator.  At least one employee will be

either present on the facility premises or on call with responsibility for coordinating all

emergency response measures at all times.  The primary and secondary coordinators are

thoroughly familiar with all aspects of the facility’s contingency plan, all operations and

activities at the facility, the location and characteristics of materials handled, the location

of all records within the facility, and the facility layout.  In addition, these coordinators

have the authority to commit the resources needed to carry out the contingency plan.

5.4	EMERGENCY RESPONSE AGENCIES AND TEAM MEMEBERS

The agencies and response team members to be notified whenever an imminent or actual

Emergency occurs are presented on page iii, located at the beginning of Section 5.

5.5	ACTIONS OF THE EMERGENCY COORDINATOR

Whenever there is an imminent or actual emergency situation, the emergency coordinator

(or the designee when the emergency coordinator is on call) must immediately:

- Notify all facility personnel present of the emergency.  The size of this facility makes direct verbal communication or use of the intercom system the most expedient form of emergency notification.  The emergency coordinator may also elect to proceed to the front of the building and repeatedly sound a car horn to notify building occupants of an emergency.  A head count will be performed by the emergency coordinator.

______________________________________________________________________________

5-7

Revision 0 – 06/30/10

- Notify appropriate state or local agency with designated response roles if their help is needed.

- Summon the primary emergency coordinator if they are not present.

Whenever a release, fire, or explosion occurs the emergency coordinator must immediately identify the character, exact source, amount, and the extent of any released materials.  Due to the limited types of chemicals in storage, the identification process can easily be performed visually.

Procedure for Assessing Possible Hazard to the Environment and Human Health

- After identification of the character, source, amount, and extent of a release, fire, or explosion the emergency coordinator must decide whether the situation can be contained and cleaned up by Branch personnel and equipment.

- If it is determined that the event is uncontrollable by Branch personnel, or is threatening neighboring establishments or population, assistance from local emergency response agencies shall be summoned immediately and an evacuation order requested.

- In the event of a release outside the containment area that is deemed immediately uncontainable or unrecoverable, local emergency response agencies and/or emergency response contractors shall be called in for assistance.

- After termination of a fire, explosion, or release outside of containment an evaluation of whether or not residues in the form of gas or liquid have become airborne, seeped into ground water, and/or reached surface water bodies will be made.

- Expert assistance should be requested to determine whether the escaped materials are potentially harmful and whether the receiving medium ultimately will be a populated area, public water supply, private well, or an environmentally sensitive area.

- Additional steps shall then be taken to mitigate the potential impact on the environment and human health, in accordance with expert recommendations.

______________________________________________________________________________

5-8

Revision 0 – 06/30/10

If the emergency coordinator determines that the facility has had a release, fire, explosion

or other emergency that could threaten human health, or the environment the coordinator

must report those findings as follows:

- If the assessment indicates that evacuation of local areas may be advisable, the coordinator must immediately notify appropriate authorities.  The coordinator must be available to help officials decide whether local area should be evacuated.

- The coordinator must immediately notify the Southeast District of the FDEP, at (561) 681-6600 during regular business hours, or the State Warning Point at (850) 413-9911 outside regular business hours or holidays, or the National Response Center at (800) 424-8802 by telephone.

A written report must be completed including:

  - Name and telephone number of notifier;

  - Name and address of facility;

  - Time and type of incident (e.g., release, fire, explosion);

  - Name and quantity of material(s) involved, to the extent known;

  - The extent of injuries, if any; and

  - The possible hazards to human health, or the environment outside the facility.

Immediate assistance in assessing and responding to an emergency is obtained by the emergency coordinator by calling the 24-hour Safety-Kleen emergency number (800) 468-1760.  This number is managed by Infotrac, a vendor contracted by Safety-Kleen to respond to all reports of spills, or chemical emergencies.  All Safety-Kleen facilities in the State of Florida utilize this contractual agreement with Infotrac.  This allows Safety-Kleen to respond to any emergency with maximum effort, thereby reducing the threat to human health and the environment.

During an emergency, the emergency coordinator must take all reasonable measures necessary to ensure that fires, explosions, and releases do not occur, recur, or spread to other hazardous waste present at the facility.

______________________________________________________________________________

5-9

Revision 0 – 06/30/10

These measures must include, where applicable, stopping processes and operations,

collecting and containing released waste, and removing or isolating containers.

If the facility stops operations in response to a fire, explosion, or release, the emergency

coordinator must monitor for leaks, pressure build-up, gas generation, or ruptures in

valves, pipes, or other equipment, wherever this is appropriate.

Immediately following an emergency, the emergency coordinator must provide for

treating, storing, or disposing of recovered waste, contaminated soil or surface water, or

any other material that results from a release, fire, or explosion at the facility.

The emergency coordinator must ensure that, in the affected area(s) of the facility:

- No waste that may be incompatible with the released material is treated or stored until cleanup procedures are completed; and

- All emergency equipment listed in the contingency plan is cleaned and fit for its intended use before operations are resumed.

The owner or operator must notify the appropriate state and local authorities that the facility is in compliance with the requirements of the preceding paragraph, before operations are resumed in the affected area(s) of the facility.

The owner or operator must note in the operating record the time, date, and details of any incident that requires implementing the contingency plan.  Within 15 days after an incident that requires implementing the contingency plan the owner/operator must submit a written report to the Southeast District of the FDEP, 400 North Congress Avenue, Suite 200, West Palm Beach, FL 33401.  This report must include:

- Name, address, and telephone number of owner/operator;

- Name, address, and telephone number of facility;

- Date, time, and type of incident (e.g., fire, release, explosion);

- Name and quantity of material(s) involved;

______________________________________________________________________________

5-10

Revision 0 – 06/30/10

- The extent of injuries, if any;

- An assessment of actual or potential hazards to human health or the environment, where this is applicable; and

- Estimated quantity and disposition of recovered material that resulted from the incident.

5.6	POTENTIAL SPILL SOURCES

The following is a list of activities that have the potential for a small scale (less than 55

gallons of waste) pollution incident.

- Moving of containers – Every time a container is moved the possibility exists that it could tip over or be dropped.  To minimize the possibility of spillage of solvent under those conditions, all container lids must be secured before the container is moved.

- Delivery truck container transfers.

  - Individual delivery containers hold from 5 to 55 gallons of waste, a quantity which can be contained by absorbent pads, if accidentally spilled.

  - Each vehicle is equipped with a hand cart and either a lift gate or hoist for ease of moving clean solvent containers off the truck and into the customers shop and returning the dirty solvent containers to the truck.

  - Lids are secured on containers during movement to prevent a spill.

  - Each truck contains a complete spill kit, shovel, and a quantity of sorbent material to contain minor spills.

  - The cargo must be secured in the route vehicle before transit.

______________________________________________________________________________

5-11

Revision 0 – 06/30/10

Spills Inside Buildings

In the event of a spill indoors, the doors and windows should be opened to improve the

ventilation in the confined area.  Following the instructions of the Material Safety Data

Sheet (MSDS), a worker would enter the area wearing rubber gloves, boots, respirator,

and safety glasses.  He or she would then mop up the liquid and place into drum(s) for

disposal.  The cleanup is completed when the workers have cleaned themselves and the

emergency equipment with soap and water.

Spills on Concrete Pads

Concrete pads in loading and unloading areas are, in most cases, equipped with

secondary containment.  Under most spill conditions, product can be totally contained

on the concrete surface and in the containment system.  Upon containment, arrangements

must be immediately undertaken to recover the material.  Any soil that may be involved

must be removed and handled in the same manner as the material spilled.

Tank Spills or Leakage

Aboveground Storage Tanks are underlain by a concrete slab and surrounded by a

concrete dike to contain any spilled or leaked solvent.  The containment system has been

sized in accordance with the regulations, and the product will be totally contained under

most spill conditions.  Should a spill occur, arrangements must be immediately

undertaken to recover the material.  In the event of leakage, tank repair or replacement

will be initiated.  Any soil that may be involved must be removed and handled in the

same manner as the material spilled.

______________________________________________________________________________

5-12

Revision 0 – 06/30/10

Spill Control Procedures

If a discharge occurs:

1.	Stop the discharge, if possible, by immediately transferring the liquid to a good

container.

2.	Retain, contain, or slow the flow of material, if possible, by diking with sorbent

pad or dirt.  Based on the seriousness of the incident, the emergency coordinator

will select the level of personal protective equipment required to address the

incident.  Pump and mop up the liquid from the floor into a good container and

return the container to storage for subsequent shipment to a Safety-Kleen recycle

center for reclamation/disposal.  The area and equipment that comes in contact

with the spill must be decontaminated with soap and water.  All residues

resulting from containment and decontamination must be collected for proper

disposal.

3.	If the material escapes the containment efforts, immediately call the cleanup

contractor with response time less than two hours (page iii).  Record date, time,

and name of person taking the message.  Call the primary emergency coordinator

if that person is absent.

4.	Immediately recover spilled solvent to reduce property and environmental

damage using the emergency and safety equipment available onsite for such

situations (Figure 5.6-1 and Table 5.6-1), or call in emergency response

contractors (page iii).  Start recovery operations immediately.

After recovery of spilled solvent, wash all contaminated impervious surfaces and

equipment with soap and water.  The residue of spill, or fire contaminated soils

and waste waters must be removed and disposed of at a Safety-Kleen recycle

center.  In addition, the recovered solvent will be sent to a Safety-Kleen recycle

center for reclamation.

______________________________________________________________________________

5-13

Revision 0 – 06/30/10

5.	Report any incident as soon as possible to the 24-hour Safety-Kleen emergency

line at (800) 468-1760.  If a representative of Safety-Kleen’s Environmental

Department does not respond within 30 minutes, the emergency coordinator

should call the State Warning Point (850) 413-9911, or the National Response

Center (800) 424-8802.

6.	The person reporting a spill should be prepared to give their name, position,

company name, address, and telephone number.  The person reporting also

should give the nature of the material spilled (e.g., immersion cleaner, etc.) and

if possible, an estimate of the amount, and whether it is near surface water or

could enter surface water by flowing through ditches or storm sewers.

If assistance is needed, the emergency coordinator should describe the containment status

and specify any additional equipment needed.  When reporting a spill, record the date and

time of the call and the name of the person answering the call at the above number.

Spill prevention plans are reviewed with facility personnel every year, and records of the

Training are kept at the facility.

Information on every spill must be recorded on the (Safety-Kleen Incident Report Form,

Figure 5.6-2 or similar).  A notification of each spill will be sent to the Corporate

Environmental Department.

Reports of emergency incidents will be sent to the FDEP or designee within 15 days of

occurrence.  This report shall include:

1.	Name, address, and telephone number of the owner/operator;

2.	Name, address, and telephone number of the facility;

3.	Date, time, and type of incident (e.g., fire, spill, explosion);

4.	Name and quantity of materials involved;

5.	The extent of injuries, if any;

______________________________________________________________________________

5-14

Revision 0 – 06/30/10

6.	An assessment of actual or potential hazards to human health or the environment,

where this is applicable; and

7.	Estimated quantity and disposition of recovered material that resulted from the

incident.

Containment Systems

Containerized Wastes

Containers are stored in the container storage area.  The storage area is totally contained

by a sloped concrete floor and collection trench (Figure 5.6-3).  Any small spill that

might occur would drain to the collection trench.  The containment system is free of

cracks.  Containers are stored on pallets whenever possible.

In the container storage area, containers are handled with a forklift and/or hand-truck free

of sharp points.  Every time a container is moved, the possibility exists that it will be

tipped over, dropped, or punctured.  To minimize the possibility of spillage, container

lids are secured and containers are kept in an upright position.  A small portable electric

pump is available to quickly transfer the liquid from ay leaking container into a safe

container.  Each route truck is equipped with a lift gate or an electric hoist.  The

appropriate device is used in the loading/unloading operation to minimize chances for

spillage and/or employee injury.  Containerized wastes at the Boynton Beach facility are

loaded/unloaded in the vicinity of the contained concrete dock on the south side of the

building (Figure 5.1-2).

Because the container storage area is fully enclosed, spills originating in this area

should not come in contact with storm water.

All containers are covered during movement and are located within diked, concrete

floored areas to contain any potential spill.

______________________________________________________________________________

5-15

Revision 0 – 06/30/10

The small quantities of waste onsite at any time can be cleaned up immediately through

the use of hand-held electric pumps, mops, wet/dry vacuums, or sorbent materials should

a spill occur.  Any spilled waste is contained for offsite recycling/reclamation.

All containerized waste movement is performed manually by a pallet jack, or propane-

fueled forklift truck.  Therefore, power outages are not expected to threaten employee

safety.

Return/Fill Station

The return/fill station (Figure 5.6-4) is a covered, grated dock with concrete pads and

curbing.  Sloping of the containment area is essentially non-detectable.  However, there

is a slight slope toward the sump.  Delivery trucks are positioned in the containment

area during loading/unloading.  Any spills which occur on the concrete are cleaned up and the area decontaminated.  The decontamination process should result in de minimus amounts of residue remaining.

All traffic areas are covered by either concrete or asphalt, thus preventing direct contact

with soils and ground water.

Tank Area

The tank area (Figure 5.6-5) houses five tanks within an enclosed building, and is

provided with containment.  The foundation slab is surrounded by a 36” concrete dike.

Tankers used for offloading/loading park on the concrete pad south of the tank area.  Any

leaks or spills at the tanker connections will be removed by absorbent or by wet

vacuuming.

______________________________________________________________________________

5-16

Revision 0 – 06/30/10

Employee training emphasizes the importance of inspection, maintenance, personal

safety, and reporting of conditions with pollution incident potential.  This training,

coupled with Safety-Kleen’s containment system and immediate cleanup of any spills,

will greatly minimize, or eliminate the chance of contamination of ground water and/or

surface water in the vicinity of the site.  Surface run-off at the site does not come in

contact with stored products or wastes in the waste management areas.

5.7	DECONTAMINATION

Once the spilled material has been cleaned up, the spill area and equipment used during

the spill clean-up must be decontaminated and/or disposed, as described below.

Concrete Surfaces/Containment Area

- Concrete surfaces/containment areas will be cleaned with a detergent solution and then rinsed with water.  The rinsate will be collected via wet vacuums and placed in containers.  Visual inspection will be use to determine the success of the decontamination process.

- The intent of the surface decontamination is to prevent current or future releases of materials to the environment.  Vigorous cleaning with detergent is sufficient to prevent releases to the environment during normal operations.  Potential for hazards from residual materials to future occupants of the facility are addressed in the closure plans for the facility and the decontamination procedures incorporated therein.

Equipment

The equipment used clean the area includes mops, pails, scrub brushes, and a wet/dry

vacuum.  Equipment which is considered reusable (i.e., pails, wet/dry vacuum, hoses)

will be washed with detergent, and wash water and rinsate will be collected for proper

________________________________________________________________________

5-17

Revision 0 –06/30/10

disposal.  All non-reusable equipment and/or equipment which is not capable of being

decontaminated will be containerized and disposed of as hazardous waste.

Wash Water and Rinsate

If the rinsate or other wastes generated in the clean-up process is determined to be hazardous, it will be properly disposed of as a hazardous waste; otherwise, the material will be disposed of as an industrial waste.  It should be noted that wash water and rinsate will not be allowed to drain to surface waters.

5.8	EMERGENCY RESPONSE EQUIPMENT AND COMMUNICATION

Due to the small size of the facility, routine communication will be accomplished by

verbal communication.  Emergency alarms are available at the tank farm, return/fill

station, and warehouse.  Telephones are used in case of a spill or fire emergency to

summon assistance.  Emergency numbers are posted by phones throughout the facility.

Included with these phone numbers is the 24-hour Safety-Kleen Emergency Reporting

number.  Figure 5.6-1 provides the locations of fire extinguishers, first aid kits, and

emergency eyewash stations.  Other emergency response equipment (Table 5.6-1) is

kept in a small storage area inside the warehouse near the return/fill station.  This

equipment includes mops, buckets, soap, shovels, and spill sorbent pads.  Rubber gloves,

boots, pumps, and a wet/dry vacuum cleaner are stored in an emergency supply area near

the container storage area.  Descriptions and uses of the equipment are provided in Table

5.8-1.  The City of Boynton Beach supplies water for domestic use, decontamination, and

fire fighting.  Adequate aisle space is provided in the container storage area for

movement in an emergency situation.

Pails, hoses, and detergents are the primary equipment that will be used for

decontamination.  The equipment available at the facility for emergency situations is

adequate for most cases.

______________________________________________________________________________

5-18

Revision 0 – 06/30/10

Large or serious emergency situations will be remediated by local emergency response

teams or special emergency response or cleanup contractors.  The facility is constructed

and operates in accordance with National Fire Protection Association (NFPA) standards

and applicable local ordinances.  Applicable health and safety standards are also observed

at the Branch.

5.9	FIRE CONTROL PROCEDURES

In the event of a fire at the facility, the following activities will be executed:

- Call the Fire Department (page iii).  (Note:  Center aisles are available in the container storage area to permit fire department personnel to pass freely with fire fighting equipment.)

- Act quickly with fire extinguishers to put out the fire before it spreads.

- Call the Police Department (page iii) to maintain traffic and on-lookers.

- Call the local hospital (page iii) to notify the type and extent of injuries, if any.

Areas within the Branch building (offices, return/fill station, container storage area) and the storage building have automatic fire fighting sprinkler systems (Figure 5.9-1).  In addition, building walls have a four-hour fire rating.

PROCEDURES IN THE EVENT OF EXPLOSION

In the event of an imminent or actual explosion at the facility, the following activities will be executed:

- All facility personnel and visitors will be notified via the intercom system or direct verbal notification to immediately evacuate the premises.  (A head count will be taken by the emergency coordinator at the designated gathering point to

- ensure everyone has been accounted for)

____________________________________________________________________

5-19

Revision 0 – 06/30/10

- The Fire & Police Departments will be immediately notified of the event by calling the respective phone numbers on page iii of this plan via the 911 emergency number.

- Based on his knowledge of the facility the emergency coordinator will try to ascertain the location of the explosion and materials involved. Also he/she will provide the emergency responders an updated copy of the facility’s hazardous material inventory list (This list is updated on a daily basis and an updated copy kept at the entrance lobby of the facility).

- If there are any injuries requiring medical assistance the local hospital (page iii) will be immediately notified as to the type and extent.

Ignitable Wastes

All wastes and products are kept away from ignition sources.  Personnel must confine smoking and open flames to remote areas (smoking is designated in the front of the office building), separate from any solvent, or ignitable wastes – products.  The tank farm is more than 20 feet from the property line.  Likewise, the flammable storage area is 50 feet or more from the property line.  Both of these distances meet the NFPA code for storage of ignitable materials.

Ignitable wastes are handled so that they do not:

1.	Become subject to extreme heat or pressure, fire of explosion, or violent reaction.

The parts washer solvents and paint wastes are stored in a tank or in containers,

none of which are near sources of extreme heat, fire, potential explosion sources

or subject to violent reactions.  The tanks are vented and the containers kept at

room temperature to minimize the potential for pressure build-up.

______________________________________________________________________________

5-20

Revision 0 – 06/30/10

2.	Produce uncontrolled toxic mists, fumes, dusts, or gases in quantities sufficient to

threaten human health.  The vapor pressure of petroleum-based parts washer

solvent is low (2 mm mercury) and may, along with paint waste, react with

strong oxidizers and reactive metals only.  Toxic mists, fumes, and dusts do not

form in quantities sufficient to threaten human health since strong oxidizers are

not handled at this facility and the solvent vaporization is minimal under normal

working conditions.  (Note:  Dry-cleaning wastes are initially not flammable, but

may produce toxic gases and hydrochloric acid at elevated temperatures (about

1,200 ° F).)

3.	Produce uncontrolled fires or gases in quantities sufficient to pose a risk of fire or

explosion – See “1” above and “4” below.

4.	Damage the structural integrity of the Safety-Kleen facility – The parts washer

solvent and paint wastes do not cause deterioration of the tank, drums, or other

structural components of the facility.

Incompatible Wastes

Incompatible wastes are segregated in an appropriate manner at the facility in accordance

with industry standards.  All waste or products are kept away from ignition sources.

Employees must confine smoking or open flames to designated safe areas.

Materials are handled so they do not:

a.	Generate extreme heat or pressure, fire or explosion, or violent reaction.

b.	Produce uncontrolled toxic mists, fumes, dusts, or gases in sufficient quantities to

threaten human health.

c.	Produce uncontrolled fires or gases in sufficient quantities to pose a risk of fire or

explosion.

d.	Damage the structural integrity of the Safety-Kleen facility.

______________________________________________________________________________

5-21

Revision 0 – 06/30/10

Adequate aisle space is maintained to allow unobstructed movement of personnel, fire

protection equipment, and decontamination equipment to any area of the facility

operation in an emergency.

External Factors

The design of the facility is such that a harmful spill is highly unlikely to occur from

most external factors.  The storage tanks are inaccessible to non-Safety-Kleen personnel.

Also, the container storage area is in a building which is inaccessible to unauthorized

personnel.

1.	Vandalism – Only extreme vandalism would result in a solvent spill or fire.

Responses to spills and fires are described in a previous section of this plan.

2.	Strikes – A strike would not result in a solvent spill or fire.

3.	Power Failure – A power failure would not result in a spill or fire.  Should a

power failure occur, all activities requiring electricity will cease.

4.	Flooding – The waste management facility elevation is above the projected 100-

year flood plain; therefore, a 100-year flood will not affect the facility.

5.	Storms or Cold Weather – The solvent return/fill station, tank storage, and the

container storage area are covered to eliminate the possibility of rain entering

the waste management areas.  Neither snow, cold weather, nor storm water is

expected to affect the facility.

5.10	EVACUATION PLAN

In the event of an uncontrollable emergency, all persons are to be evacuated from the area

by means of a verbal cry or use of the public address system and are to assemble across

from the entrance drive to the facility to assure that all personnel are accounted for and

out of harms way.  Clearly marked exits exist in the warehouse and office areas.  The emergency coordinator may elect to use a car horn as a means of emergency notification.

________________________________________________________________________

5-22

Revision 0 – 06/30/10

A head count will be performed by the emergency coordinator at the assembly area.

The Fire Department must be notified at the time of evacuation from a safe onsite building

or neighboring facility.

5.11	AVAILABILITY AND REVISION OF THE PREPAREDNESS, PREVENTION, AND

CONTINGENCY PLAN

This Plan and all revisions to it are kept at the facility and regularly updated throughout

the operating life of the facility.

Copies of this document are provided to local authorities and organizations listed under

the Preparedness and Prevention Plan, which may be called upon to provide emergency

assistance.

This Plan and all revisions to it are made readily available to employees working at the

facility.

This Plan is reviewed and updated, if necessary, whenever:

- The facility permit is modified to allow new process wastes to be stored or treated, or applicable regulations are revised;

- The list or location of emergency equipment changes

- The facility changes in its design, construction, operation, maintenance, or other circumstances in a way that:

  - Materially increases the potential for fires, explosions, or releases of hazardous waste or hazardous waste constituents, or

  - Changes in the response necessary in an emergency.

- The names, addresses, or phone numbers of emergency coordinators change;

- The employee assigned to each emergency task changes, or

____________________________________________________________________

5-23

Revision 0 – 06/30/10

- The plan fails when implemented in an emergency.

5.12	ARRANGEMENTS WITH LOCAL AUTHORITIES

Arrangements have been made to familiarize the Fire Department, Police Department, and

local emergency response teams with the layout of the facility, properties of hazardous

materials handled (Material Safety Data Sheets) at the facility and associated hazards,

places where facility personnel would normally be working, entrances to and roads inside

the facility, and possible evacuation routes.

Potential primary and secondary response contractors are identified in this Plan.

Arrangements have been made to familiarize the local hospital with the properties of

hazardous waste handled at the facility and the types of injuries or illnesses which would

result from fires, explosions, or releases at the facility.

Appendix A of this Plan (located at the end of Section 5) includes copies of example

distribution letters for transmittal.  Copies of updated transmittal letters are kept on file

at the facility.

______________________________________________________________________________

5-24