EXHIBIT I

KEENE ROAD SOUTH LANDFILL

WACS_FACILITY:  87081

MONITORING PLAN IMPLEMENTATION SCHEDULE

(REVISED 04/17/06)

GENERAL

1.	The permittee must initiate implementation of this Monitoring Plan within ninety (90) days from the date of permit issuance.  [62-701.510(1)(b)&(c), 62-522.600(5), Florida Administrative Code (F.A.C.)]

2.	The field testing, sample collection and preservation and laboratory testing, including quality control procedures, shall be in accordance with Chapter 62-160 Florida Administrative Code (F.A.C.).  Approved methods as published by the Department or as published in Standard Methods, ASTM, or EPA Methods shall be used.  [62-701.510(2)(b), F.A.C.]

3.	The organization collecting samples at this site must use the Field and Laboratory Standard Operating Procedures (DEP-SOP-001/01) in Chapter 62-160, F.A.C.  Sampling personnel must have a copy of the SOP for purging and sampling in the field when sampling and must be knowledgeable of its contents, procedures, and forms.  The laboratory designated to conduct the chemical analyses must be certified by the Florida Department of Health Environmental Laboratory Certification Program (DoH ELCP).  This Certification must be for the test method and analyte(s) that are reported.  [62-160.210(1), 62-160.320(1), F.A.C.]

NOTE:  DEP-SOP-001/01 can be accessed at: http://www.dep.state.fl.us/labs/qa/sops.htm

4.	If, at any time, analyses detect parameters which are significantly above background water quality, or which are at levels above the Department’s water quality standards or criteria specified in Chapter 62-520, F.A.C., in the detection wells or at the edge of the Zone of Discharge, the Permittee shall resample the wells within thirty (30) days after the sampling data are received, to confirm the data.  Should the permittee choose not to resample, the Department will consider the water quality analysis as representative of current ground water conditions at the facility.  If the data are confirmed, or if the permittee chooses not to resample, the permittee shall notify the Department in writing within 14 days of this finding.  Upon notification by the Department, the permittee shall initiate evaluation monitoring in accordance with Rule 62-701.510(7) F.A.C.  [62-701.510(7)(a), F.A.C.]

GROUND WATER QUALITY MONITORING

5.	The fifty (50) ground water monitoring wells designated for water quality testing and water level measurements are listed on Attachment A and are shown on Attachment B.  [62-701.510(3)(d)2 & 3, F.A.C.]

NOTE:  Unless otherwise approved by the Department, wells with high turbidities must be remediated or reinstalled to reduce the turbidity value to less than 20 NTU prior to sample collection.  Should any ground water sample exhibit dissolved oxygen concentrations greater than 20% of oxygen saturation at the field measured temperature, the sampled well must be repurged then resampled as soon as an acceptable dissolved oxygen value has been attained unless it can be demonstrated that in situ ground water contains higher levels of dissolved oxygen.  All water quality analyses will be performed on unfiltered samples unless approved by the Department.

6.	Initial samples collected from MW-9A, MW-9B, MW-11A, MW-11B, MW-14A, MW-14B, MW-15A, MW-15B, MW-FL5 and MW-FL6 shall be analyzed and reported before the Department grants approval for solid waste disposal in cells 5-8.

Initial samples collected from MW-10A, MW-10B, MW-12A, MW-12B MW-13A, MW-13B, MW-16A, MW-16B MW-17A, MW-17B, MW-18A, MW-18B, MW-19A, MW-19B, MW-20A, MW-20B MW-21A, MW-21B, MW-FL4, MW-FL7, MW-FL8 and MW-FL9 shall be analyzed and reported before the Department grants approval for solid waste disposal in cells 9-12.  The samples shall be analyzed for the list of Initial Ground Water Parameters on Attachment C.  [62-701.510(6)(b)2, F.A.C.]

7.	Semi-annual samples from MW-1A, MW-1B, MW-2A, MW-2B, MW-3A, MW-3B, MW-4A, MW-4B, MW-5A, MW-5B, MW-6A, MW-6B, MW-7A, MW-7B, MW-8, MW-FL1, MW-FL2 and MW-FL3 shall be collected June and December when solid waste disposal begins in Cells 1-4.

Semi-annual samples from MW-9A, MW-9B, MW-11A, MW-11B, MW-14A, MW-14B, MW-15A, MW-15B, MW-FL5 and MW-FL6 shall be collected in June and December when solid waste disposal begins in Cells 5-8.

Semi-annual samples from MW-10A, MW-10B, MW-12A, MW-12B MW-13A, MW-13B, MW-16A, MW-16B MW-17A, MW-17B, MW-18A, MW-18B, MW-19A, MW-19B, MW-20A, MW-20B MW-21A, MW-21B, MW-FL4, MW-FL7, MW-FL8 and MW-FL9 shall be collected when solid waste disposal begins in Cells 9-12.  The samples shall be analyzed for the list of Semi-Annual Ground Water Parameters on Attachment D.  [62-701.510(1)(a)2, 62-701.510(8)(a), F.A.C.]

Please confer with your consultant and analytical laboratory prior to sampling to ensure the analytical method is capable of achieving detection limits at or below the Ground Water Cleanup Target Levels (GCTLs) in Chapter 62-777, F.A.C.  GCTLs are used as screening tools and interim guidelines for ground water minimum criteria until standards are promulgated. [62-701.510(6)(b)1 & 2, 62-701.510(6)(d) & (8)(a) & (d), F.A.C.]

8.	Ground water levels in all wells, whether sampled or not, must be measured to the nearest 0.01 foot and reported semiannually unless required more frequently by permit condition.  All water level measurements must be made within a one-day period.  These measurements must be referenced to the National Geodetic Vertical Datum of 1929 (NGVD).  [62-701.510(9)(a), F.A.C.]

# MONITORING WELL REQUIREMENTS

9.	Installation of new monitoring wells MW-9A, MW-9B, MW-11A, MW-11B, MW-14A, MW-14B, MW-15A, MW-15B, MW-FL5 and MW-FL6 shall commence within ninety (90) days before the placement of waste in Cells 5-8.

Installation of new monitoring wells MW-10A, MW-10B, MW-12A, MW-12B MW-13A, MW-13B, MW-16A, MW-16B MW-17A, MW-17B, MW-18A, MW-18B, MW-19A, MW-19B, MW-20A, MW-20B MW-21A, MW-21B, MW-FL4, MW-FL7, MW-FL8 and MW-FL9 shall commence within ninety (90) days before the placement of waste in Cells 9-12.  [62-701.510(1)(b) & (c), 62-522.600(5), F.A.C.]

10.	If a monitoring well becomes damaged or inoperable, the Permittee shall notify the Department in writing within seven (7) days.  The written report shall describe what problem has occurred and the remedial measures that have been taken to prevent a recurrence.  The Department can require the replacement of inoperable monitoring wells.  [62-4.070(3), F.A.C.]

11.	New or replacement monitoring well design or placement must be approved by the Department.  Proposed well construction details based on site-specific borings must be submitted with all supporting data (grain size distribution analyses, in-situ hydraulic conductivity testing, depth to water, etc.) for Department approval prior to well installation.  Use of hollow stem auger equipment is recommended.  Other drilling methods must be approved by the Department prior to well installation.  [62-522.600(3), F.A.C.]

12.	All wells shall be clearly and permanently labeled and the well site maintained so that the well is visible at all times. Protective barriers must be installed at all wells that may be subject to damage by heavy equipment or traffic.  [62-701.510(3)(d)2, F.A.C.]

13.	An abandonment plan for abandoning any well that is unsuitable for ground water monitoring must be approved by the Department prior to abandonment.  [62-701.510(3)(d)5, F.A.C.]

# REPORTING REQUIREMENTS

# GENERAL

14.	The Department must be notified in writing at least fourteen (14) days prior to the installation and/or sampling of any monitoring well(s).  [62-701.510(9)(a), F.A.C.]

15.	One paper copy of Attachment E, Monitoring Well Completion Report Form, must be submitted to the Department within thirty (30) days after installation of new or replacement monitoring wells.  NOTE:  the top of casing elevation of each well, to an accuracy of 0.01 feet, and the latitude and longitude of each well in degrees, minutes and seconds, to two (2) decimal places, with an accuracy of 15 feet, must be determined and certified by a Florida Licensed Surveyor and Mapper and provided on the form.  In addition, as built well construction diagrams and soil boring logs that cover the entire depth of the monitoring well(s) must be submitted to the Department.  [62-701.510(3)(d)1, 62-532.410, 62-4.070(3), F.A.C.]

16.	A drawing must be submitted within thirty (30) days following monitoring well installation showing the location of all monitoring wells (active and abandoned), water bodies and waste filled areas.  The location of features on the drawing must be horizontally and vertically located by standard surveying techniques.  The drawing shall include all monitoring well locations, each monitoring well name and identification (WACS) number, the top of casing, pad elevation, permanent benchmark(s) and/or corner monument marker(s) referenced to NGVD with an accuracy of 0.01 feet.  The latitude and longitude of each well in degrees, minutes and seconds, to two (2) decimal places, with an accuracy of 15 feet, must be determined and provided on the drawing. The survey shall be conducted and certified by a Florida Licensed Surveyor and Mapper  [701.510(1)(c), 62-701.510(3)(d) 1, F.A.C.]

17.	A total depth measurement must be made on all wells at time of permit renewal.  This measurement is to be reported as total apparent depth below ground surface and should be compared to the original total depth of the well.
[62-701.510(1)(c), F.A.C.]

INITIAL AND SEMI-ANNUAL

18.	Required monitoring reports must be submitted to the Department within sixty (60) days of receipt of analysis from the laboratory.  There are two options for submitting water quality data, paper or electronic.  [62-701.730(4)(b), 62-4.070(3), F.A.C.]

Paper Only Reporting: One (1) copy of the monitoring report shall be submitted at the required time.  The report shall include documents as listed in Table 1.

Electronic Laboratory Analysis Reporting: One (1) copy of the paper portion of a monitoring report shall be submitted at the required time along with the disc containing the water quality data as listed in Table 1.  The data required on the disc is listed on ftp://ftp.dep.state.fl.us/pub/labs/lds/validator/validator_fields.pdf.

To decrease the need for resubmittal you may evaluating data prior to submittal at http://www.floridadep.org/labs/software/index.htm.

A sample text file may be viewed at http://www.dep.state.fl.us/labs/software/sampledata.txt

Interpretative documents such as exceedence summary and/or contour maps must be certified by a professional licensed in state of Florida whose expertise is related to the document.

Table 1.  Reporting Requirements

| Documents | Paper report | Electronic Report* |
| --- | --- | --- |
| Sampling notification | Paper or electronic | Paper or electronic |
| Cover letter | Paper | Paper |
| Summary of exceedences and recommendations | Paper | Paper |
| Ground water contour maps | Paper | Paper |
| Survey drawings | Paper | Paper |
| Lab certification report form (Attachment F) | Paper | Paper |
| Field data sheets/sampling logs (Attachment G) | Paper | Paper |
| Chain of custody | Paper | Paper |
| Water levels –water elevation table | Paper | Paper |
| Total depth measurements | Paper | Paper |
| Lab quality control report | Paper | Paper |
| Lab data sheets | Paper | Not applicable** |
| DEP parameters report forms | Paper | Not applicable** |
| Lab data in Excel tab-delimited format compatible with Validator, plus the same spread sheet in pdf form | Not applicable | Electronic |

*Electronic Compact disc media readable by a Microsoft Windows computer

**The tab-delimited text file on the disc replaced these documents

19.	Water levels in all monitoring wells, whether sampled or not, must be measured to the nearest 0.01 foot and reported semi-annually unless required more frequently by permit condition.  All water level measurements must be made within a one-day period.  These measurements should be reported in a table that includes well or surface water point name, date water level measured, measuring point elevation referenced to NGVD, depth to water and calculated water level elevation referenced to NGVD.  [62-701.510(9)(a)8, F.A.C.]

20.	A ground water elevation contour map for each monitored aquifer zone must be submitted semi-annually to the Department.  Ground water elevation contour map(s) should include monitoring well locations, ground water elevation at each monitoring well location referenced to NGVD, a bar scale, ground water contour interval, date of measurement and ground water flow direction.  The map(s) must incorporate adjacent and on-site surface water elevations where appropriate.  These maps shall be signed and sealed pursuant to Florida Statutes (F.S.) Chapters 471 and 492 which require that documents requiring the practice of professional engineering or professional geology, as described in Chapter 471 or 492, F.S., be signed and sealed by the professional(s) who prepared or approved them.  This certification must be made by a licensed professional who is able to demonstrate competence in this subject area.  [62-701.510(9)(a)9, F.A.C.]

BIENNIAL

21.	One paper copy of a technical report shall be submitted to the Department every two years, and shall be updated at the time of permit renewal.  The report shall summarize and interpret the water quality data and water level measurements collected during the past four years.  The report shall contain, at a minimum, the following:

a.	Tabular and graphical displays of any data that shows that a monitoring parameter has been detected, including hydrographs for all monitoring wells.

b.	Trend analyses of any monitoring parameters detected.

c.	Comparisons among shallow, middle, and deep zone wells.

d.	Comparison between upgradient and downgradient wells.

e.	Correlation between related parameters such as total dissolved solids and specific conductance.

f.	Discussion of erratic and/or poorly correlated data.

g.	An interpretation of the ground water contour maps, including an evaluation of ground water flow rates.

h.	An evaluation of the adequacy of the water quality monitoring frequency and sampling locations based upon site conditions.

This report must be signed and sealed pursuant to Florida Statutes (F.S.) Chapters 471 and 492 which require that documents requiring the practice of professional engineering or professional geology, as described in Chapter 471 or 492, F.S., be signed and sealed by the professional(s) who prepared or approved them.  This certification must be made by a licensed professional who is able to demonstrate competence in the subject area(s) addressed within the sealed document.  [62-701.510(9)(b), F.A.C.]

List of Attachments

Attachment A - Well List

##### Attachment B - Map

Attachment C - Initial Ground Water Parameters

Attachment D - Semi-annual Ground Water Parameters

Attachment E - Monitoring Well Completion Form

Attachment F - Ground Water Monitoring Report Form

##### Attachment G - Water Sampling Form