EXHIBIT I

TOMOKA FARMS ROAD LANDFILL

WACS_FACILITY:  27540

MONITORING PLAN IMPLEMENTATION SCHEDULE

GENERAL

1.	The permittee must initiate implementation of this Monitoring Plan within ninety (90) days from the date of permit issuance.  [62-701.510(1)(b)&(c), 62-522.600(5), Florida Administrative Code (F.A.C.)]

2.	The field testing, sample collection and preservation and laboratory testing, including quality control procedures, shall be in accordance with Chapter 62-160 Florida Administrative Code (F.A.C.).  Approved methods as published by the Department or as published in Standard Methods, ASTM, or EPA Methods shall be used.  [62-701.510(2)(b), F.A.C.]

3.	The organization collecting samples at this site must use the Field and Laboratory Standard Operating Procedures (DEP-SOP-001/01) in Chapter 62-160, F.A.C.  Sampling personnel must have a copy of the SOP for purging and sampling in the field when sampling and must be knowledgeable of its contents, procedures, and forms.  The laboratory designated to conduct the chemical analyses must be certified by the Florida Department of Health Environmental Laboratory Certification Program (DoH ELCP).  This Certification must be for the test method and analyte(s) that are reported.  [62-160.210(1), 62-160.320(1), F.A.C.]

NOTE:  DEP-SOP-001/01 can be accessed at http://www.dep.state.fl.us/labs/qa/sops.htm

- If, at any time, analyses detect parameters which are significantly above background water quality, or which are at levels above the Department’s water quality standards or criteria specified in Chapter 62-520, F.A.C., in the detection wells or at the edge of the Zone of Discharge, the Permittee shall resample the wells within thirty (30) days after the sampling data are received, to confirm the data.  Should the permittee choose not to resample, the Department will consider the water quality analysis as representative of current ground water conditions at the facility.  If the data are confirmed, or if the permittee chooses not to resample, the permittee shall notify the Department in writing within 14 days of this finding.  Upon notification by the Department, the permittee shall initiate evaluation monitoring in accordance with Rule 62-701.510(7) F.A.C.  [62-701.510(7)(a), F.A.C.]

NOTE:  As stated in Chapter 62-520, F.A.C., the water quality standard for arsenic will decrease to 0.010 mg/l on January 1, 2005.

GROUND WATER QUALITY MONITORING

5.	The fifty-four (54) ground water monitoring wells designated for water quality testing and water level measurements are listed on Attachment A and shown on Attachment B.  [62-701.510(3)(d)2 & 3, F.A.C.]

NOTE:  Unless otherwise approved by the Department, wells with high turbidities must be remediated or reinstalled to reduce the turbidity value to less than 20 NTU's prior to sample collection.  Should any ground water sample exhibit dissolved oxygen concentrations greater than 20% of oxygen saturation at the field measured temperature, the sampled well must be repurged then resampled as soon as an acceptable dissolved oxygen value has been attained unless it can be demonstrated that in situ ground water contains higher levels of dissolved oxygen.  All water quality analyses will be performed on unfiltered samples unless approved by the Department.

6.	Samples from the fifty-four (54) ground water monitoring wells shall be collected semi-annually and analyzed as follows: water elevation, specific conductivity (field), pH (field), dissolved oxygen (field), turbidity (field), temperature (field), colors and sheens (by observation), total ammonia as N, chlorides, iron, mercury, nitrate, sodium, total dissolved solids (TDS), and the parameters listed in 40 CFR Part 258  Appendix I.  [62-701.510(1)(a)2, 62-701.510(8)(a), F.A.C.]

Please confer with your consultant and analytical laboratory prior to sampling to ensure the analytical method is capable of achieving detection limits at or below the Ground Water Cleanup Target Levels (GCTLs) in Chapter 62-777, F.A.C.

NOTE:  GCTLs are used as screening tools and interim guidelines for ground water minimum criteria until standards are promulgated.

7.	Ground water levels in all wells, whether sampled or not, must be measured to the nearest 0.01 foot and reported semiannually unless required more frequently by permit condition.  All water level measurements must be made within a one-day period.  These measurements must be referenced to the National Geodetic Vertical Datum of 1929 (NGVD)  [62-701.510(9)(a), F.A.C.]

SURFACE WATER MONITORING

8.	The ten (10) surface water sites included in this monitoring plan are SW-1, SW-2, SW-3, SW-4, SW-5, SW-6, SW-9, SW-10, SW-11 AND SW-12.  They are listed on Attachment A and shown on Attachment B..  [62-701.510(4)(c), F.A.C.]

the Ground Water Cleanup Target Levels (GCTLs) in Chapter 62-777, F.A.C.

9.	Samples from the ten (10) surface water monitoring sites shall be collected semi-annually and analyzed as follows: water elevation, specific conductivity (field), pH (field), dissolved oxygen (field), turbidity (field), temperature (field), colors and sheens (by observation), unionized ammonia (NH3), total hardness as CaCO3, biochemical oxygen demand (5 day), copper, iron, mercury, nitrate, zinc, total dissolved solids (TDS), total organic carbon (TOC), fecal coliform, total phosphates, chlorophyll A, total nitrogen, chemical oxygen demand (COD), total suspended solids (TSS), and the parameters listed in 40 CFR, Part 258 Appendix I.  [62-701.510(6)(e) & (8)(b), F.A.C.]

Please confer with your consultant and analytical laboratory prior to sampling to ensure the analytical method is capable of achieving detection limits at or below the Ground Water Cleanup Target Levels (GCTLs) in Chapter 62-777, F.A.C.

NOTE:  GCTLs are used as screening tools and interim guidelines for ground water minimum criteria until standards are promulgated.

10.	Surface water elevations at sampling locations and must be measured to the nearest 0.01 foot on the same day as ground water levels in the wells and reported semiannually unless required more frequently by permit condition.  All water level measurements must be made within a one-day period.  These measurements must be referenced to NGVD.  [62-701.510(9)(a)8, F.A.C.]

LEACHATE QUALITY MONITORING

11.	The site designated for leachate quality testing is L-1.  The site is listed on Attachment A and shown on Attachment B.  [62-701.510(5), F.A.C.]

12.	Samples from the leachate monitoring site shall be collected annually and analyzed as follows: specific conductivity (field), pH (field), dissolved oxygen (field), colors and sheens (by observation), total ammonia as N, bicarbonate, chlorides, iron, mercury, nitrate, sodium, total dissolved solids (TDS) and the parameters listed in 40 CFR Part 258, Appendix II.

If the annual analysis indicates that a contaminant listed in 40 CFR Part 261.24 exceeds the regulatory level listed therein, the permittee shall initiate monthly sampling and analysis and shall notify the Department in writing.  If in any three consecutive months no listed contaminant is found to exceed the regulatory level, the permittee may discontinue the monthly sampling and analysis and return to a routine sampling schedule.  [62-701.510(6)(c)1 & 2, F.A.C.]

# MONITORING WELL REQUIREMENTS

13.	If a monitoring well becomes damaged or inoperable, the Permittee shall notify the Department in writing within seven (7) days.  The written report shall describe what problem has occurred and the remedial measures that have been taken to prevent a recurrence.  The Department can require the replacement of inoperable monitoring wells.  [62-4.070(3), F.A.C.]

14.	New or replacement monitoring well design or placement must be approved by the Department.  Proposed well construction details based on site-specific borings must be submitted with all supporting data (grain size distribution analyses, in-situ hydraulic conductivity testing, depth to water, etc.) for Department approval prior to well installation.  Use of hollow stem auger equipment is recommended.  Other drilling methods must be approved by the Department prior to well installation.  [62-522.600(3), F.A.C.]

15.	All wells shall be clearly and permanently labeled and the well site maintained so that the well is visible at all times. Protective barriers must be installed at all wells that may be subject to damage by heavy equipment or traffic.  [62-701.510(3)(d)2, F.A.C.]

16.	An abandonment plan for abandoning any well that is unsuitable for ground water monitoring must be approved by the Department prior to abandonment.  [62-701.510(3)(d)5, F.A.C.]

# REPORTING REQUIREMENTS

GENERAL

17.	The Department must be notified in writing at least fourteen (14) days prior to the installation and/or sampling of any monitoring well(s).  [62-701.510(9)(a), F.A.C.]

18.	Well completion reports for new monitoring wells must be submitted to the Department on the Ground Water Monitoring Well Completion Report Form (attached) thirty (30) days after installation.  Note that the top of casing elevation of each well, to an accuracy of 0.01 feet, and the latitude and longitude of each well in degrees, minutes and seconds, to two (2) decimal places, with an accuracy of 15 feet, must be determined and certified by a Florida Licensed Surveyor and Mapper and provided on the form.  In addition, as built well construction diagrams and soil boring logs that cover the entire depth of the monitoring well(s) must be submitted to the Department.
[62-701.510(3)(d)1, 62-532.410, 62-4.070(3), F.A.C.]

- A drawing must be submitted within thirty (30) days following monitoring well installation showing the location of all monitoring wells (active and abandoned), water bodies and waste filled areas.  The location of features on the drawing must be horizontally and vertically located by standard surveying techniques.  The drawing shall include all monitoring well locations, each monitoring well name and identification (WACS) number, the top of casing, pad elevation, permanent benchmark(s) and/or corner monument marker(s) referenced to NGVD with an accuracy of 0.01 feet.  The latitude and longitude of each well in degrees, minutes and seconds, to two (2) decimal places, with an accuracy of 15 feet, must be determined and provided on the drawing. The survey shall be conducted and certified by a Florida Licensed Surveyor and Mapper  [701.510(1)(c), 62-701.510(3)(d) 1, F.A.C.]

20.	A total depth measurement must be made on all wells at time of permit renewal.  This measurement is to be reported as total apparent depth below ground surface and should be compared to the original total depth of the well.
[62-701.510(1)(c), F.A.C.]

SEMI-ANNUAL

21.	The required monitoring results must be submitted to the Department within sixty (60) days of receipt from the laboratory. There are two options for reporting monitoring results.  [62-701.510(9)(a), F.A.C.]

- Paper Reporting: The Parameter Report Forms for initial and semi-annual monitoring are attached.  In order to facilitate entry of this data into the State computer system (WACS), these forms or exact replicas must be used and must not be altered as to content.  The original copies of the forms should be retained so that the necessary information is available to properly complete future reports. The submittal shall also include Ground Water Monitoring Report (attached), laboratory reports with quality assurance information, Chain of Custody sheets, water sampling log (attached), ground water contour maps, a summary of any water quality standards or minimum criteria that are exceeded, and recommended corrective action.  Interpretative document such as exceedance summary and/or contour maps must be certified by a professional licensed in state of Florida whose expertise is related to the document.

2.	Electronic Reporting:  The Department has developed computer software, called Validator to evaluate monitoring data and transfer the data into the Department computer database.   Electronic data management saves time and reduces costs.  It also eliminates errors generated by manual data input.  The data and other related information are prepared in Microsoft Excel and saved as a tab-delimited text file.

In order to maintain integrity of electronic data, the Department asks that two (2) copies of electronic data files be submitted on compact disc media readable by a Microsoft Windows computer.  One should be in a tab-delimited text file and one should be in portable document format (PDF).  Details on how to complete the text file for electronic processing is presented in Table 1.

We encourage you to use Validator to evaluate the electronic data, and make any necessary revisions or corrections before submittal to the Department.  Preparation of a text file as outlined in Table I enables the Validator to function.

A sample text file may be viewed at:  http://www.dep.state.fl.us/labs/software/sampledata.txt

### Table 1. Electronic Laboratory Data Submittal Fields for Validator/WACS Upload

| Field Name | Description |
| --- | --- |
| WACS_Facility | WACS ID used to identify site where data will be uploaded. Information may be obtained from Monitoring Plan issued by the Department. |
| Project | Proper name for facility used to confirm WACS ID. Information may be obtained from Monitoring Plan issued by the Department. |
| WACS_Well | WACS ID used to identify specific testsite (Well, Leachate, Surface Water, etc). Information may be obtained from Monitoring Plan issued by the Department. |
| Monitoring_Site_Num | Testsite designation relevant to the sample (MW-1, SW-1, Leachate sump, etc). Use "DUP" after the well name and its test site I.D. that duplicates are obtained, e.g. MW-2DUP and/or 15334DUP. Information may be obtained from Monitoring Plan issued by the Department. |
| WACS_Report_Type | Used to identify type of report (Semiannual GW, Annual Leachate, etc), see code table. Information may be obtained from Monitoring Plan issued by the Department. |
| Ground_Water_Class | Used to identify GW or SW classes (G-I1, G-III, SW-I, LC, etc), see code table. Information may be obtained from Monitoring Plan issued by the Department. |
| Well_Type | Used to identify type of well (Background, Compliance, Detection, etc), see code table. Information may be obtained from Monitoring Plan issued by the Department. |
| Well_Purge_Flag | Used to confirm well purging prior to sampling (Y or N) (may be blank for SW, leachate). |
| GW_Elevation | For ground water elevation use STORET codes 082545 or 072020, Ana_Method is "DEP-SOP", Qualifier is "D". |
| Samp_Method | Method used to collect the sample (grab, bailer, peristaltic pump, etc), see code table. |
| Date_Sampled | Date sample was collected. Make sure analysis dates for field parameters, e.g. pH, dissolved oxygen, temperature, conductivity, turbidity and water elevation are the same as sampling date. |
| DOHE | DOH certification number for laboratory. For field parameters, e.g. pH, dissolved oxygen, temperature, conductivity, turbidity and water elevation, DOHE is "DEP-SOP" in place of using the NELAC certification number. |
| Sample_Id | Assigned by lab to each sample for QC purposes. |
| Matrix | Type of matrix (W= water/liquid, S= soil/sediment/solid waste). |
| Filtered | Used to identify filtered samples (Y or N). |
| Date_Prepared | Date sample was prepared for analysis, if required (may be blank). |
| Preservation | Method used to preserve sample (cool to 4oC, pH<2, etc) (may be blank). |
| Preservation_Intact | Indicates condition received at lab (Y or N). |
| Date_Analyzed | Date lab analysis was conducted for sample. |
| Ana_Method | EPA method used to analyze sample (EPA 8260). |
| Storet_Code | Appropriate STORET parameter code, must be six digits (039430 for Isodrin). |
| Parameter | Name of compound analyzed (Benzene, Arsenic, etc) or measured in field (pH, DO, etc). |
| Result | Numeric results of analysis, do not include non-numeric characters such as < or >. Only numeric numbers are allowed in the result and detection limit columns. Use the qualifier column to specify results and detection limits. |
| Units | Units corresponding to analytical results (mg/l, ug/l, etc). Use either "U" or "u" for microgram. |
| Detection_Limit | MDL (not PQL) for analytical method, (may be blank for field parameters). Only numeric numbers are allowed in the result and detection limit columns. Use the qualifier column to specify results and detection limits. |
| Qualifier | Appropriate data qualifiers as listed in 62-160, FAC (may be blank), see code table. |
| Comment | Any additional comments on the sample (may be blank). |
| CAS-Number | Chemical Abstract Service Registry Number (may be blank), optional. |

Notes:

- All dates are reported in the following format where HH is the hours on the 24 hour clock. MM/DD/YYYY HH:MM:SS

- We encourage you to utilize Validator to validate and evaluate EDD prior to submittal. By doing so will eliminate the Department returning the submitted EDD for correction. To download Validator software, go to http://www.floridadep.org/labs/software/index.htm.

- A complete list of Storet Codes, Parameter names and Chemical Abstract Service Registry Numbers (CAS-RNs), or a single query of these fields may be viewed at http://www.floridadep.org/labs/cgi-bin/wacs/search.asp

Supporting documentation such as ground water report certifications (attached), laboratory reports with quality assurance information, Chain of Custody sheets, water sampling logs (attached), ground water contour maps, a summary of any water quality standards or minimum criteria that are exceeded, and any recommended corrective action must be submitted.  Supporting document may be scanned and submitted electronically in lieu of a paper copy.  To maintain integrity of electronic submittal, document must be submitted in portable document format (PDF).  Interpretative document such as exceedence summary and/or contour maps must be certified by a professional registered in state of Florida who is able to demonstrate competence in this subject area.  A document with a legible seal that can be scanned may be submitted electronically.
[62-701.510(9)(a), F.A.C.]

22.	Water levels in all monitoring wells, whether sampled or not, and all surface water sites must be measured to the nearest 0.01 foot and reported semi-annually unless required more frequently by permit condition.  All water level measurements must be made within a one-day period.  These measurements should be reported in a table that includes well or surface water point name, date water level measured, measuring point elevation referenced to NGVD, depth to water and calculated water level elevation referenced to NGVD.
[62-701.510(9)(a)8, F.A.C.]

23.	A ground water elevation contour map for each monitored aquifer zone must be submitted semi-annually to the Department.  Ground water elevation contour map(s) should include monitoring well locations, ground water elevation at each monitoring well location referenced to NGVD, a bar scale, ground water contour interval, date of measurement and ground water flow direction.  The map(s) must incorporate adjacent and on-site surface water elevations where appropriate.  These maps shall be signed and sealed pursuant to Florida Statutes (F.S.) Chapters 471 and 492 which require that documents requiring the practice of professional engineering or professional geology, as described in Chapter 471 or 492, F.S., be signed and sealed by the professional(s) who prepared or approved them.  This certification must be made by a licensed professional who is able to demonstrate competence in this subject area.  [62-701.510(9)(a)9, F.A.C.]

BIENNIAL

24.	One copy of a technical report shall be submitted to the Department every two years, and shall be updated at the time of permit renewal.  The report shall summarize and interpret the water quality data and water level measurements

collected during the past four years.  The report shall contain, at a minimum, the following:

a.	Tabular and graphical displays of any data that shows that a monitoring parameter has been detected, including hydrographs for all monitoring wells.

b.	Trend analyses of any monitoring parameters detected.

c.	Comparisons among shallow, middle, and deep zone wells.

d.	Comparison between upgradient and downgradient wells.

e.	Correlation between related parameters such as total dissolved solids and specific conductance.

f.	Discussion of erratic and/or poorly correlated data.

g.	An interpretation of the ground water contour maps, including an evaluation of ground water flow rates.

h.	An evaluation of the adequacy of the water quality monitoring frequency and sampling locations based upon site conditions.

This report must be signed and sealed pursuant to Florida Statutes (F.S.) Chapters 471 and 492 which require that documents requiring the practice of professional engineering or professional geology, as described in Chapter 471 or 492, F.S., be signed and sealed by the professional(s) who prepared or approved them.  This certification must be made by a licensed professional who is able to demonstrate competence in the subject area(s) addressed within the sealed document.  [62-701.510(9)(b), F.A.C.]