| Parameter No./Name (refers to parameter number on Tables IA,B, C, D,E, F, G & H as noted) | Container | Preservation, | Maximum holding time |
| --- | --- | --- | --- |
| Table IA—Bacterial Tests: |  |  |  |
| 1–5. Coliform, total, fecal, and E. coli | PA, G | Cool, <10 °C, 0.0008% Na2S2O3 | 6 hours, |
| 6. Fecal streptococci | PA, G | Cool, <10 °C, 0.0008% Na2S2O3 5 | 6 hours6 |
| 7. Enterococci | PA, G | Cool, <10 °C, 0.0008% Na2S2O3 5 | 6 hours6 |
| 8. Salmonella | PA, G | Cool, <10 °C, 0.0008% Na2S2O3 5 | 6 hours6 |
| Table IA— Aquatic Toxicity Tests: |  |  |  |
| 9–11. Toxicity, acute and chronic | P, FP, G | Cool, ≤6 °C | 36 hours |
| Table lB—Inorganic Tests: |  |  |  |
| 1. Acidity | P, FP, G | Cool, ≤6 °C | 14 days |
| 2. Alkalinity | P, FP, G | Cool, ≤6 °C9 | 14 days |
| 4. Ammonia | P, FP, G | Cool, ≤6 °C9, H2SO4 to pH<2 | 28 days |
| 9. Biochemical oxygen demand | P, FP, G | Cool, ≤6 °C9 | 48 hours |
| 10. Boron | P, FP, or Quartz | HNO3 to pH<2 | 6 months |
| 11. Bromide | P, FP, G | None required | 28 days |
| 14. Biochemical oxygen demand, carbonaceous | P, FP G | Cool, ≤6 °C9 | 48 hours |
| 15. Chemical oxygen demand | P, FP, G | Cool, ≤6 °C9, H2SO4 to pH<2 | 28 days |
| 16. Chloride | P, FP, G | None required | 28 days |
| 17. Chlorine, total residual | P, G | None required | Analyze within 15 minutes |
| 21. Color | P, FP, G | Cool, ≤6 °C9 | 48 hours |
| 23–24. Cyanide, total or available (or CATC) | P, FP, G | Cool, ≤6 °C9, NaOH to pH>12, reducing agent 5 | 14 days |
| 25. Fluoride | P | None required | 28 days |
| 27. Hardness | P, FP, G | HNO3 or H2SO4 to pH<2 | 6 months |
| 28. Hydrogen ion (pH) | P, FP, G | None required | Analyze within 15 minutes |
| 31, 43. Kjeldahl and organic N | P, FP, G | Cool, ≤6 °C9, H2SO4 to pH<2 | 28 days |
| Table IB—Metals: |  |  |  |
| 7 18. Chromium VI | P, FP, G | Cool, ≤6 °C9, pH = 9.3–9.7 | 28 days |
| 35. Mercury (CVAA) | P, FP, G | HNO3 to pH<2 | 28 days |
| 35. Mercury (CVAFS) | FP, G; and FP-lined cap13 | 5 mL/L 12N HCl or 5 mL/L BrCl | 90 days13 |
| 3, 5–8, 12, 13, 19, 20, 22, 26, 29, 30, 32–34, 36, 37, 45, 47, 51, 52, 58–60, 62, 63, 70– 72, 74, 75. Metals, except boron, chromium VI, and mercury. | P, FP, G | HNO3 to pH<2, or at least 24 hours prior to analysis | 6 months |
| 38. Nitrate | P, FP, G | Cool, ≤6 °C9 | 48 hours |
| 39. Nitrate-nitrite | P, FP, G | Cool, ≤6 °C9, H2SO4 to pH<2 | 28 days |
| 40. Nitrite | P, FP, G | Cool, ≤6 °C9 | 48 hours |
| 41. Oil and grease | G | Cool, ≤6 °C9, HCl or H2SO4 to pH<2 | 28 days |
| 42. Organic Carbon | P, FP, G | Cool, ≤6 °C9, HCl, H2SO4, or H3PO4 to pH<2. | 28 days |
| 44. Orthophosphate | P, FP, G | Cool, ≤6 °C9 | Filter within 15 minutes; Analyze within 48 hours |
| 46. Oxygen, Dissolved Probe | G, Bottle and top | None required | Analyze within 15 minutes |
| 47. Winkler | G, Bottle and top | Fix on site and store in dark | 8 hours |
| 48. Phenols | G | Cool, ≤6 °C9, H2SO4 to pH<2 | 28 days |
| 49. Phosphorous (elemental) | G | Cool, ≤6 °C9 | 48 hours |
| 50. Phosphorous, total | P, FP, G | Cool, ≤6 °C9, H2SO4 to pH<2 | 28 days |
| 53. Residue, total | P, FP, G | Cool, ≤6 °C9 | 7 days |
| 54. Residue, Filterable | P, FP, G | Cool, ≤6 °C9 | 7 days |
| 55. Residue, Nonfilterable (TSS) | P, FP, G | Cool, ≤6 °C9 | 7 days |
| 56. Residue, Settleable | P, FP, G | Cool, ≤6 °C9 | 48 hours |
| 57. Residue, Volatile | P, FP, G | Cool, ≤6 °C9 | 7 days |
| 61. Silica | P or Quartz | Cool, ≤6 °C9 | 28 days |
| 64. Specific conductance | P, FP, G | Cool, ≤6 °C9 | 28 days |
| 65. Sulfate | P, FP, G | Cool, ≤6 °C9 | 28 days |
| 66. Sulfide | P, FP, G | Cool, ≤6 °C9, add zinc acetate plus sodium hydroxide to pH>9 | 7 days |
| 67. Sulfite | P, FP, G | None required | Analyze within 15 minutes |
| 68. Surfactants | P, FP, G | Cool, ≤6 °C9 | 48 hours |
| 69. Temperature | P, FP, G | None required | Analyze |
| 73. Turbidity | P, FP, G | Cool, ≤6 °C9 | 48 hours |
| Table lC—Organic Tests 8 |  |  |  |
| 13, 18–20, 22, 24–28, 34–37, 39–43, 45–47, 56, 76, 104, 105, 108–111, 113. Purgeable Halocarbons | G, FP-lined septum | Cool, ≤6 °C9, 0.008% Na2S2O3 5 | 14 days |
| 6, 57, 106. Purgeable aromatic hydrocarbons | G, FP-lined septum | Cool, ≤6 °C9, 0.008% Na2S2O3 5, HCl to pH 2 | 14 days16 |
| 3, 4. Acrolein and acrylonitrile | G, FP-lined septum | Cool, ≤6 °C9, 0.008% Na2S2O3 5, pH to 4–5 | 14 days17 |
| 23, 30, 44, 49, 53, 77, 80, 81, 98, 100, 112. Phenols | G, FP-lined cap | Cool, ≤6 °C9, 0.008% Na2S2O3 5 | 7 days until extraction, 40 days after extraction |
| 7, 38. Benzidines 18, | G, FP-lined cap | Cool, ≤6 °C9, 0.008% Na2S2O3 5 | 7 days until extraction |
| 14, 17, 48, 50–52. Phthalate esters 18 | G, FP-lined cap | Cool, ≤6 °C9 | 7 days until extraction, 40 days after extraction |
| 82–84. Nitrosamines 18, | G, FP-lined cap | Cool, ≤6 °C9, store in dark, 0.008% Na2S2O3 5 | 7 days until extraction, 40 days after extraction |
| 88–94. PCBs18 | G, FP-lined cap | Cool, ≤6 °C9 | 1 year until extraction, 1 year after extraction |
| 54, 55, 75, 79. Nitroaromatics and isophorone18 | G, FP-lined cap | Cool, ≤6 °C9, store in dark, 0.008% Na2S2O3 5 | 7 days until extraction, 40 days after extraction |
| 1, 2, 5, 8–12, 32, 33, 58, 59, 74, 78, 99, 101. Polynuclear aromatic hydrocarbons18 | G, FP-lined cap | Cool, ≤6 °C9, store in dark, 0.008% Na2S2O3 5 | 7 days until extraction, 40 days after extraction |
| 15, 16, 21, 31, 87. Haloethers18 | G, FP-lined cap | Cool, ≤6 °C9, 0.008% Na2S2O3 5 | 7 days until extraction, 40 days after extraction |
| 29, 35–37, 63–65, 107. Chlorinated hydrocarbons18 | G, FP-lined cap | Cool, ≤6 °C9 | 7 days until extraction, 40 days after extraction |
| 60–62, 66–72, 85, 86, 95–97, 102, 103. CDDs/CDFs18 |  |  |  |
| Aqueous Samples: Field and Lab Preservation | G | Cool, ≤6 °C9, 0.008% Na2S2O3 5, pH<9 | 1 year |
| Solids and Mixed-Phase Samples: Field Preservation | G | Cool, ≤6 °C9 | 7 days |
| Tissue Samples: Field Preservation | G | Cool, ≤6 °C9 | 24 hours |
| Solids, Mixed-Phase, and Tissue Samples: Lab Preservation | G | Freeze, ≤-10 °C | 1 year |
| Table lD—Pesticides |  |  |  |
| Tests: 1–70. Pesticides18 | G, FP-lined cap | Cool, ≤6 °C9, pH 5–9 | 7 days until extraction, 40 days after extraction |
| Table IE—Radiological Tests: |  |  |  |
| 1–5. Alpha, beta, and radium | P, FP, G | HNO3 to pH<2 | 6 months |
| Table IH—Bacterial Tests: |  |  |  |
| 1. E. coli | PA, G | Cool, <10 °C, 0.008% Na2S2O3 5 | 6 hours6 |
| 2. Enterococci | PA, G | Cool, <10 °C, 0.008% Na2S2O3 5 | 6 hours6 |
| Table IH—Protozoan Tests: |  |  |  |
| 8. Cryptosporidium | LDPE; field filtration | 0–8 °C | 96 hours. |
| 9. Giardia | LDPE; field filtration | 0–8 °C | 96 hours23 |

Reference:  This table is adapted from Federal Register, Vol. 72, No. 57, Monday, March 20, 2007 pp 14230-14233

| Analyte | Methods | Reference | Container | Preservation | Maximum Holding Time |
| --- | --- | --- | --- | --- | --- |
| Bromine | DPD Colorimetric | SM 4500-Cl-G | P, G | None required | Analyze immediately |
| Bromates | Ion Chromatography | EPA 300.0 | P, G | Cool 4°C | 30 days |
| Chlorophylls | Spectrophotometric | SM 10200 H | P, G | Dark 4°C Filtered, dark, -20°C | 48 hours chilled until filtration, and analyze immediately or 48 hours chilled until filtration8,and 28 days (frozen)after filtration |
| Corrosivity | Calculated (CaCO3 Stability, Langelier Index) | SM 2330 ASTM D513-92 | P, G | Cool 4°C | 7 days9 |
| FL-PRO | Gas Chromatography | DEP (11/1/95) | G only | Cool 4°C, H2SO4 or HCl to pH<2 | 7 days until extraction, 40 days after extraction |
| Odor | Human Panel | SM 2150 | G only | Cool 4°C | 6 hours |
| Salinity | Electrometric Hydrometric10 | SM 2520 B SM 2520 C | G, wax seal | Analyze immediately or use wax seal | 30 days10 |
| Taste | Human Panel | SM 2160 B, C, D ASTM E679-91 | G only | Cool 4°C | 24 hours |
| Total Dissolved Gases | Direct-sensing Membrane-diffusion | SM 2810 | __________ | ___________ | Analyze in-situ |
| Total Petroleum Hydrocarbons | Gravimetry | EPA 1664 | G only | Cool 4°C, H2SO4 or HCl to pH<2 | 28 days |
| Transparency | Irradiometric | 62-302.200(6), FAC | __________ | ___________ | Analyze in-situ |
| Un-ionized Ammonia | Calculated | DEP-SOP | P, G | Cool 4°C Na2S2O3 12 | 8 hours unpreserved 28 days preserved 12 |
| Organic Pesticides | GC and HPLC | EPA (600-series) 14 |  | 15 | 15 |

# Comments

Add a reducing agent only if an oxidant (e.g., chlorine) is present. Reducing agents shown to be effective are sodium thiosulfate (Na2S2O3), ascorbic acid, sodium arsenite (NaAsO2), or sodium borohydride (NaBH4). However, some of these agents have been shown to produce a positive or negative cyanide bias, depending on other substances in the sample and the analytical method used. Therefore, do not add an excess of reducing agent. Methods recommending ascorbic acid (e.g., EPA Method 335.4) specify adding ascorbic acid crystals, 0.1–0.6 g, until a drop of sample produces no color on potassium iodide (KI) starch paper, then adding 0.06 g (60 mg) for each liter of sample volume. If NaBH4 or NaAsO2 is used, 25 mg/L NaBH4 or 100 mg/L NaAsO2 will reduce more than 50 mg/L of chlorine (see method ‘‘Kelada-01’’ and/or Standard Method 
4500–CN- for more information). After adding reducing agent, test the sample using KI paper, a test strip (e.g. for chlorine, SenSafeTM Total Chlorine Water Check 480010) moistened with acetate buffer solution (see Standard Method 4500–Cl.C.3e), or a chlorine/oxidant test method (e.g., EPA Method 330.4 or 330.5), to make sure all oxidant is removed. If oxidant remains, add more reducing agent. Whatever agent is used, it should be tested to assure that cyanide results are not affected adversely.

To achieve the 28-day holding time, use the ammonium sulfate buffer solution specified in EPA Method 218.6. The allowance in this footnote supersedes preservation and holding time requirements in the approved hexavalent chromium methods, unless this supersession would compromise the measurement, in which case requirements in the method must be followed.

EPA 281.6

7.9 Buffer Solution- Dissolve 33 g of ammonium sulfate in 75 mL of ASTM Type I

water and add 6.5 mL of ammonium hydroxide. Dilute to 100 mL with ASTM

Type I water.

8.2 For the determination of dissolved Cr(VI), the sample should be filtered

through a 0.45 um filter. Use a portion of the sample to rinse the syringe

filtration unit and filter and then collect the required volume of filtrate. Adjust

the pH of the sample to 9-9.5 by adding dropwise a solution of the buffer,

periodically checking the pH with the pH meter.

Add a reducing agent only if an oxidant (e.g., chlorine) is present. Reducing agents shown to be effective are sodium thiosulfate (Na2S2O3), ascorbic acid, sodium arsenite (NaAsO2), or sodium borohydride (NaBH4). However, some of these agents have been shown to produce a positive or negative cyanide bias, depending on other substances in the sample and the analytical method used. Therefore, do not add an excess of reducing agent. Methods recommending ascorbic acid (e.g., EPA Method 335.4) specify adding ascorbic acid crystals, 0.1–0.6 g, until a drop of sample produces no color on potassium iodide (KI) starch paper, then adding 0.06 g (60 mg) for each liter of sample volume. If NaBH4 or NaAsO2 is used, 25 mg/L NaBH4 or 100 mg/L NaAsO2 will reduce more than 50 mg/L of chlorine (see method ‘‘Kelada-01’’ and/or Standard Method 
4500–CN- for more information). After adding reducing agent, test the sample using KI paper, a test strip (e.g. for chlorine, SenSafeTM Total Chlorine Water Check 480010) moistened with acetate buffer solution (see Standard Method 4500–Cl.C.3e), or a chlorine/oxidant test method (e.g., EPA Method 330.4 or 330.5), to make sure all oxidant is removed. If oxidant remains, add more reducing agent. Whatever agent is used, it should be tested to assure that cyanide results are not affected adversely.

If the sample is not adjusted to pH 2, then the sample must be analyzed within seven days of sampling.

The pH adjustment is not required if acrolein will not be measured. Samples for acrolein receiving no pH adjustment must be analyzed within 3 days of sampling.

The pH adjustment may be performed upon receipt at the laboratory and may be omitted if the samples are extracted within 72 hours of collection. For the analysis of aldrin, add 0.008% Na2S2O3.

# Endnotes

‘‘P’’ is polyethylene; ‘‘FP’’ is fluoropolymer (polytetrafluoroethylene (PTFE; Teflon®), or other fluoropolymer, unless stated otherwise in this Table II; ‘‘G’’ is glass; ‘‘PA’’ is any plastic that is made of a sterlizable material (polypropylene or other autoclavable plastic); ‘‘LDPE’’ is low density polyethylene.

Except where noted in this Table II and the method for the parameter, preserve each grab sample within 15 minutes of collection. For a composite sample collected with an automated sampler (e.g., using a 24-hour composite sampler; see 40 CFR 122.21(g)(7)(i) or 40 CFR Part 403, Appendix E), refrigerate the sample at ≤6 °C during collection unless specified otherwise in this Table II or in the method(s). For a composite sample to be split into separate aliquots for preservation and/or analysis, maintain the sample at ≤6 °C, unless specified otherwise in this Table II or in the method(s), until collection, splitting, and preservation is completed. Add the preservative to the sample container prior to sample collection when the preservative will not compromise the integrity of a grab sample, a composite sample, or an aliquot split from a composite sample; otherwise, preserve the grab sample, composite sample, or aliquot split from a composite sample within 15 minutes of collection. If a composite measurement is required but a composite sample would compromise sample integrity, individual grab samples must be collected at prescribed time intervals (e.g., 4 samples over the course of a day, at 6-hour intervals). Grab samples must be analyzed separately and the concentrations averaged. Alternatively, grab samples may be collected in the field and composited in the laboratory if the compositing procedure produces results equivalent to results produced by arithmetic averaging of the results of analysis of individual grab samples. For examples of laboratory compositing procedures, see EPA Method 1664A (oil and grease) and the procedures at 40 CFR 141.34(f)(14)(iv) and (v) (volatile organics).

When any sample is to be shipped by common carrier or sent via the U.S. Postal Service, it must comply with the Department of Transportation Hazardous Materials Regulations (49 CFR Part 172). The person offering such material for transportation is responsible for ensuring such compliance. For the preservation requirements of Table II, the Office of Hazardous Materials, Materials Transportation Bureau, Department of Transportation has determined that the Hazardous Materials Regulations do not apply to the following materials: Hydrochloric acid (HCl) in water solutions at concentrations of 0.04% by weight or less (pH about 1.96 or greater); Nitric acid (HNO3) in water solutions at concentrations of 0.15% by weight or less (pH about 1.62 or greater); Sulfuric acid (H2SO4) in water solutions at concentrations of 0.35% by weight or less (pH about 1.15 or greater); and Sodium hydroxide (NaOH) in water solutions at concentrations of 0.080% by weight or less (pH about 12.30 or less).

Samples should be analyzed as soon as possible after collection. The times listed are the maximum times that samples may be held before the start of analysis and still be considered valid (e.g., samples analyzed for fecal coliforms may be held up to 6 hours prior to commencing analysis). Samples may be held for longer periods only if the permittee or monitoring laboratory has data on file to show that, for the specific types of samples under study, the analytes are stable for the longer time, and has received a variance from the Regional Administrator under § 136.3(e). For a grab sample, the holding time begins at the time of collection. For a composite sample collected with an automated sampler (e.g., using a 24-hour composite sampler; see 40 CFR 122.21(g)(7)(i) or 40 CFR Part 403, Appendix E), the holding time begins at the time of the end of collection of the composite sample. For a set of grab samples composited in the field or laboratory, the holding time begins at the time of collection of the last grab sample in the set. Some samples may not be stable for the maximum time period given in the table. A permittee or monitoring laboratory is obligated to hold the sample for a shorter time if it knows that a shorter time is necessary to maintain sample stability. See § 136.3(e) for details. The date and time of collection of an individual grab sample is the date and time at which the sample is collected. For a set of grab samples to be composited, and that are all collected on the same calendar date, the date of collection is the date on which the samples are collected. For a set of grab samples to be composited, and that are collected across two calendar dates, the date of collection is the dates of the two days; e.g., November 14–15. For a composite sample collected automatically on a given date, the date of collection is the date on which the sample is collected. For a composite sample collected automatically, and that is collected across two calendar dates, the date of collection is the dates of the two days; e.g., November 14–15.

Add a reducing agent only if an oxidant (e.g., chlorine) is present. Reducing agents shown to be effective are sodium thiosulfate (Na2S2O3), ascorbic acid, sodium arsenite (NaAsO2), or sodium borohydride (NaBH4). However, some of these agents have been shown to produce a positive or negative cyanide bias, depending on other substances in the sample and the analytical method used. Therefore, do not add an excess of reducing agent. Methods recommending ascorbic acid (e.g., EPA Method 335.4) specify adding ascorbic acid crystals, 0.1–0.6 g, until a drop of sample produces no color on potassium iodide (KI) starch paper, then adding 0.06 g (60 mg) for each liter of sample volume. If NaBH4 or NaAsO2 is used, 25 mg/L NaBH4 or 100 mg/L NaAsO2 will reduce more than 50 mg/L of chlorine (see method ‘‘Kelada-01’’ and/or Standard Method 
4500–CN- for more information). After adding reducing agent, test the sample using KI paper, a test strip (e.g. for chlorine, SenSafeTM Total Chlorine Water Check 480010) moistened with acetate buffer solution (see Standard Method 4500–Cl.C.3e), or a chlorine/oxidant test method (e.g., EPA Method 330.4 or 330.5), to make sure all oxidant is removed. If oxidant remains, add more reducing agent. Whatever agent is used, it should be tested to assure that cyanide results are not affected adversely.

Samples analysis should begin immediately, preferably within 2 hours of collection. The maximum transport time to the laboratory is 6 hours, and samples should be processed within 2 hours of receipt at the laboratory.

For fecal coliform samples for sewage sludge (biosolids) only, the holding time is extended to 24 hours for the following sample types using either EPA Method 1680 (LTB–EC) or 1681 (A–1): Class A composted, Class B aerobically digested, and Class B anaerobically digested.

Sufficient ice should be placed with the samples in the shipping container to ensure that ice is still present when the samples arrive at the laboratory. However, even if ice is present when the samples arrive, it is necessary to immediately measure the temperature of the samples and confirm that the preservation temperature maximum has not been exceeded. In the isolated cases where it can be documented that this holding temperature cannot be met, the permittee can be given the option of on-site testing or can request a variance. The request for a variance should include supportive data which show that the toxicity of the effluent samples is not reduced because of the increased holding temperature.

Aqueous samples must be preserved at ≤6 °C, and should not be frozen unless data demonstrating that sample freezing does not adversely impact sample integrity is maintained on file and accepted as valid by the regulatory authority. Also, for purposes of NPDES monitoring, the specification of ‘‘≤°C’’ is used in place of the ‘‘4 °C’’ and ‘‘< 4 °C’’ sample temperature requirements listed in some methods. It is not necessary to measure the sample temperature to three significant figures (1/100th of 1 degree); rather, three significant figures are specified so that rounding down to 6 °C may not be used to meet the ≤6 °C requirement. The preservation temperature does not apply to samples that are analyzed immediately (less than 15 minutes).

Sample collection and preservation: Collect a volume of sample appropriate to the analytical method in a bottle of the material specified. If the sample can be analyzed within 48 hours and sulfide is not present, adjust the pH to > 12 with sodium hydroxide solution (e.g., 5% w/v), refrigerate as specified, and analyze within 48 hours. Otherwise, to extend the holding time to 14 days and mitigate interferences, treat the sample immediately using any or all of the following techniques, as necessary, followed by adjustment of the sample pH to > 12 and refrigeration as specified. There may be interferences that are not mitigated by approved procedures. Any procedure for removal or suppression of an interference may be employed, provided the laboratory demonstrates that it more accurately measures cyanide.  Particulate cyanide (e.g., ferric ferrocyanide) or a strong cyanide complex (e.g., cobalt cyanide) are more accurately measured if the laboratory holds the sample at room temperature and pH > 12 for a minimum of 4 hours prior to analysis, and performs UV digestion or dissolution under alkaline (pH=12) conditions, if necessary.

(1) Sulfur: To remove elemental sulfur (S8), filter the sample immediately. If the filtration time will exceed 15 minutes, use a larger filter or a method that requires a smaller sample volume (e.g., EPA Method 335.4 or Lachat Method 01). Adjust the pH of the filtrate to > 12 with NaOH, refrigerate the filter and filtrate, and ship or transport to the laboratory. In the laboratory, extract the filter with 100 mL of 5% NaOH solution for a minimum of 2 hours. Filter the extract and discard the solids. Combine the 5% NaOH-extracted filtrate with the initial filtrate, lower the pH to approximately 12 with concentrated hydrochloric or sulfuric acid, and analyze the combined filtrate. Because the detection limit for cyanide will be increased by dilution by the filtrate from the solids, test the sample with and without the solids procedure if a low detection limit for cyanide is necessary. Do not use the solids procedure if a higher cyanide concentration is obtained without it. Alternatively, analyze the filtrates from the sample and the solids separately, add the amounts determined (in μg or mg), and divide by the original sample volume to obtain the cyanide concentration.

(2) Sulfide: If the sample contains sulfide as determined by lead acetate paper, or if sulfide is known or suspected to be present, immediately conduct one of the volatilization treatments or the precipitation treatment as follows: Volatilization—Headspace expelling. In a fume hood or well-ventilated area, transfer 0.75 liter of sample to a 4.4 L collapsible container (e.g., CubitainerTM). Acidify with concentrated hydrochloric acid to pH

< 2. Cap the container and shake vigorously for 30 seconds. Remove the cap and expel the headspace into the fume hood or open area by collapsing the container without expelling the sample. Refill the headspace by expanding the container. Repeat expelling a total of five headspace volumes. Adjust the pH to > 12, refrigerate, and ship or transport to the laboratory. Scaling to a smaller or larger sample volume must maintain the air to sample volume ratio. A larger volume of air will result in too great a loss of cyanide (> 10%). Dynamic stripping: In a fume hood or well- ventilated area, transfer 0.75 liter of sample to a container of the material specified and acidify with concentrated hydrochloric acid to pH < 2. Using a calibrated air sampling pump or flowmeter, purge the acidified sample into the fume hood or open area through a fritted glass aerator at a flow rate of 2.25 L/min for 4 minutes. Adjust the pH to > 12, refrigerate, and ship or transport to the laboratory. Scaling to a smaller or larger sample volume must maintain the air to sample volume ratio. A larger volume of air will result in too great a loss of cyanide (> 10%). Precipitation: If the sample contains particulate matter that would be removed by filtration, filter the sample prior to treatment to assure that cyanide associated with the particulate matter is included in the measurement. Ship or transport the filter to the laboratory. In the laboratory, extract the filter with 100 mL of 5% NaOH solution for a minimum of 2 hours. Filter the extract and discard the solids. Combine the 5% NaOH-extracted filtrate with the initial filtrate, lower the pH to approximately 12 with concentrated hydrochloric or sulfuric acid, and analyze the combined filtrate. Because the detection limit for cyanide will be increased by dilution by the filtrate from the solids, test the sample with and without the solids procedure if a low detection limit for cyanide is necessary. Do not use the solids procedure if a higher cyanide concentration is obtained without it. Alternatively, analyze the filtrates from the sample and the solids separately, add the amounts determined (in μg or mg), and divide by the original sample volume to obtain the cyanide concentration. For removal of sulfide by precipitation, raise the pH of the sample to > 12 with NaOH solution, then add approximately 1 mg of powdered cadmium chloride for each mL of sample. For example, add approximately 500 mg to a 500-mL sample. Cap and shake the container to mix. Allow the precipitate to settle and test the sample with lead acetate paper. If necessary, add cadmium chloride but avoid adding an excess. Finally, filter through 0.45 micron filter. Cool the sample as specified and ship or transport the filtrate and filter to the laboratory. In the laboratory, extract the filter with 100 mL of 5% NaOH solution for a minimum of 2 hours. Filter the extract and discard the solids. Combine the 5% NaOH-extracted filtrate with the initial filtrate, lower the pH to approximately 12 with concentrated hydrochloric or sulfuric acid, and analyze the combined filtrate. Because the detection limit for cyanide will be increased by dilution by the filtrate from the solids, test the sample with and without the solids procedure if a low detection limit for cyanide is necessary. Do not use the solids procedure if a higher cyanide concentration is obtained without it. Alternatively, analyze the filtrates from the sample and the solids separately, add the amounts determined (in μg or mg), and divide by the original sample volume to obtain the cyanide concentration. If a ligand-exchange method is used (e.g., ASTM D6888), it may be necessary to increase the ligand-exchange reagent to offset any excess of cadmium chloride.

(3) Sulfite, thiosulfate, or thiocyanate: If sulfite, thiosulfate, or thiocyanate is known or suspected to be present, use UV digestion with a glass coil (Method Kelada-01) or ligand exchange (Method OIA–1677) to preclude cyanide loss or positive interference.

(4) Aldehyde: If formaldehyde, acetaldehyde, or another water-soluble aldehyde is known or suspected to be present, treat the sample with 20 mL of 3.5% ethylenediamine solution per liter of sample.

(5) Carbonate: Carbonate interference is evidenced by noticeable effervescence upon acidification in the distillation flask, a reduction in the pH of the absorber solution, and incomplete cyanide spike recovery. When significant carbonate is present, adjust the pH to ≥12 using calcium hydroxide instead of sodium hydroxide. Allow the precipitate to settle and decant or filter the sample prior to analysis (also see Standard Method 4500–CN.B.3.d).

(6) Chlorine, hypochlorite, or other oxidant: Treat a sample known or suspected to contain chlorine, hypochlorite, or other oxidant as directed in footnote 5.

For dissolved metals, filter grab samples within 15 minutes of collection and before adding preservatives. For a composite sample collected with an automated sampler (e.g., using a 24-hour composite sampler; see 40 CFR 122.21(g)(7)(i) or 40 CFR Part 403, Appendix E), filter the sample within 15 minutes after completion of collection and before adding preservatives. If it is known or suspected that dissolved sample integrity will be compromised during collection of a composite sample collected automatically over time (e.g., by interchange of a metal between dissolved and suspended forms), collect and filter grab samples to be composited (footnote 2) in place of a composite sample collected automatically.

To achieve the 28-day holding time, use the ammonium sulfate buffer solution specified in EPA Method 218.6. The allowance in this footnote supersedes preservation and holding time requirements in the approved hexavalent chromium methods, unless this supersession would compromise the measurement, in which case requirements in the method must be followed.

Samples collected for the determination of trace level mercury (<100 ng/L) using EPA Method 1631 must be collected in tightly-capped fluoropolymer or glass bottles and preserved with BrCl or HCl solution within 48 hours of sample collection. The time to preservation may be extended to 28 days if a sample is oxidized in the sample bottle. A sample collected for dissolved trace level mercury should be filtered in the laboratory within 24 hours of the time of collection. However, if circumstances preclude overnight shipment, the sample should be filtered in a designated clean area in the field in accordance with procedures given in Method 1669. If sample integrity will not be maintained by shipment to and filtration in the laboratory, the sample must be filtered in a designated clean area in the field within the time period necessary to maintain sample integrity. A sample that has been collected for determination of total or dissolved trace level mercury must be analyzed within 90 days of sample collection.

An aqueous sample may be collected and shipped without acid preservation. However, acid must be added at least 24 hours before analysis to dissolve any metals that adsorb to the container walls. If the sample must be analyzed within 24 hours of collection, add the acid immediately (see footnote 2). Soil and sediment samples do not need to be preserved with acid. The allowances in this footnote supersede the preservation and holding time requirements in the approved metals methods.

Guidance applies to samples to be analyzed by GC, LC, or GC/MS for specific compounds.

If the sample is not adjusted to pH 2, then the sample must be analyzed within seven days of sampling.

The pH adjustment is not required if acrolein will not be measured. Samples for acrolein receiving no pH adjustment must be analyzed within 3 days of sampling.

When the extractable analytes of concern fall within a single chemical category, the specified preservative and maximum holding times should be observed for optimum safeguard of sample integrity (i.e., use all necessary preservatives and hold for the shortest time listed). When the analytes of concern fall within two or more chemical categories, the sample may be preserved by cooling to ≤6 °C, reducing residual chlorine with 0.008% sodium thiosulfate, storing in the dark, and adjusting the pH to 6–9; samples preserved in this manner may be held for seven days before extraction and for forty days after extraction. Exceptions to this optional preservation and holding time procedure are noted in footnote 5 (regarding the requirement for thiosulfate reduction), and footnotes 19, 20 (regarding the analysis of benzidine).

If 1,2-diphenylhydrazine is likely to be present, adjust the pH of the sample to 4.0 ± 0.2 to prevent rearrangement to benzidine.

Extracts may be stored up to 30 days at < 0 °C.

For the analysis of diphenylnitrosamine, add 0.008% Na2S2O3 and adjust pH to 7–10 with NaOH within 24 hours of sampling

The pH adjustment may be performed upon receipt at the laboratory and may be omitted if the samples are extracted within 72 hours of collection. For the analysis of aldrin, add 0.008% Na2S2O3.

Holding time is calculated from time of sample collection to elution for samples shipped to the laboratory in bulk and calculated from the time of sample filtration to elution for samples filtered in the field

SM XXXX = procedures from "Standard Methods for the Examination of Water and Wastewater", APHA-AWWA-WPCF, 20th edition, 1998 and Standard Methods Online.

ASTM XXXX-YY = procedure from "Annual Book of ASTM Standards", Volumes 11.01 and 11.02 (Water I and II), 1999.

P = plastic, G = glass.

When specified, sample preservation should be performed immediately upon sample collection.

The times listed are the maximum times that samples may be held before analysis and still be considered valid.

The approved procedure is for residual chlorine.  However, in the absence of chlorine, the DPD colorimetric procedure can be adapted to measure bromine content of the sample.  In such case, the validity of this assumption must be verified by using another procedure for chlorine which is not affected by the presence of bromine (i.e., negligible interference).

The Determination of Inorganic Anions in Water by Ion Chromatography", EPA Method 300.0, Revised August 1993, by John D. Pfaff, U. S. EPA Cincinnati, Ohio 45268.

Collect samples in opaque bottles and process under reduced light.

Samples must be filtered within 48 hours of collection.  Add magnesium carbonate to the filter while the last of the sample passes through the filter..

Temperature and pH must be measured on site at the time of sample collection.  7 days is the maximum time for laboratory analysis of total alkalinity, calcium ion and total solids.

The electrometric and hydrometric analytical methods are suited for field use.  The argentometric method is suited for laboratory use.  Samples collected for laboratory analysis, when properly sealed with paraffin waxed stopper, may be held indefinitely.  The maximum holding time of 30 days is recommended as a practical regulatory limit.

Transparency in surface waters is defined as a compensation point for photosynthetic activity, i.e., the depth at which one percent of the light intensity entering at the water surface remains unabsorbed.  The DEP Chapter 62-302, FAC requires that the light intensities at the surface and subsurface be measured simultaneously by irradiance meters such as the Kahlsico Underwater Irradiometer, Model No. 268 WA 310, or an equivalent device having a comparable spectral response.

The results of the measurements of pH, temperature, salinity (if applicable) and the ammonium ion concentration in the sample are used to calculate the concentration of ammonia in the unionized state.  Temperature, pH and salinity must be measured on-site at the time of sample collection.  Laboratory analysis of the ammonium ion concentration should be conducted within eight hours of sample collection.  If prompt analysis of ammonia is impossible, preserve samples with H2SO4 to pH between 1.5 and 2.  Acid-preserved samples, stored at 4°C, may be held up to 28 days for ammonia determination.  Sodium thiosulfate should only be used if fresh samples contain residual chlorine.

DEP Central Analytical Laboratory, Tallahassee, FL, Revision No. 1, October 3, 1983.  The 1983 draft is available from the DEP Bureau of Laboratories.

Other pesticides listed in approved EPA methods (608.1, 608.2, 614, 614.1, 615, 617, 618, 619, 622, 622.1, 627, 629, 631, 632, 632.1, 633, 642, 643, 644 and 645) that are not included in Table ID of 40 CFR Part 136 (March 2007).

Container, preservation and holding time as specified in each individual method must be followed.